## Slide 1: CS 352 Network: Addressing
Lecture 19
http://www.cs.rutgers.edu/~sn624/352-F22
Srinivas Narayana

## Slide 2: Network
Application
Transport
Network
Host-to-Net
…
FTP
HTTP
SMTP
DNS
TCP
UDP
IP
802.11
X.25
ATM
HTTPS
Net layer

## Slide 3: The network layer
Main function: Move data from sending to receiving endpoint
on sending endpoint: encapsulate transport segments into datagrams
on receiving endpoint: deliver datagrams to transport layer
The network layer also runs in every router
  Very challenging to evolve the network layer
Routers examine headers on all passing through them
Network Layer
Process
Endpoint
Process
Endpoint

## Slide 4: Two key network-layer functions
Forwarding: move packets from router’s input to appropriate router output
Routing: determine route taken by packets from source to destination
  routing algorithms
The network layer solves the routing problem.
Analogy: taking a road trip
Forwarding: process of getting through single interchange
Routing: process of planning trip from source to destination
network
layer
runs
everywhere

## Slide 5: Data plane and Control Plane
Data plane = Forwarding
local, per-router function
determines how datagram arriving on router input port is forwarded to router output port
Control plane = Routing
network-wide logic
determines how datagram is routed along end-to-end path from source to destination endpoint
two control-plane approaches:
  Distributed routing algorithm running on each router
  Centralized routing algorithm running on a (logically) centralized server
0111
values in arriving
packet header
1
2
3

## Slide 6: This lecture: Addresses in the Internet
I need to send B something.
Sure, what’s B’s address?
A
B
Endpoints
Endpoints
Network layer

## Slide 7: Internet Addressing

## Slide 8: The Internet needs addresses
Addresses are a precursor to communication.
  Allow endpoints to locate each other
Internet addresses are neither endpoint names nor identify them
Addresses help routers determine how to move a packet
  Like street address for the postal system
Network layer addresses are designed to help routers perform the forwarding and routing functions efficiently
  Specifically, we’ll look at Internet Protocol (IP) addresses.
  Most popular: IP version 4 or IPv4. (later: IPv6)

## Slide 9: IPv4 Addresses
32 bits long
Identifier for a network interface
An IP address corresponds to the point of attachment of an endpoint to the network.
An IP address is NOT an identifier for the endpoint
  Changes when endpoint moves
Dotted quad notation: each byte is written in decimal in MSB order, separated by dots. Example:
10000000 11000011 00000001 01010000
128
195
1
80
.
.
.

## Slide 10: Grouping IP addresses by prefixes
IP addresses can be grouped based on a shared prefix of a specified length
Example: consider two IP addresses:
  128.95.1.80 and 128.95.1.4
  The addresses share a prefix of (bit) length 24: 128.95.1
  The addresses have different suffixes of (bit) length 8
IP addresses: prefix corresponds to the network component and the suffix to an endpoint (host) component of the address

## Slide 11: IP addresses use hierarchy to scale routing
IP addresses of endpoint interfaces in a network (e.g., Rutgers Busch campus) share a prefix of some length
Each interface/endpoint has a different suffix, and hence a different 32-bit IP address
Using prefixes reduces the amount of information needed to forward packets over the Internet
IP prefixes are like zip codes: routers don’t need to store info for each endpoint, just each prefix
Prefixes also allow IP addresses to be delegated from one network to another (more on this later)
NJ

## Slide 12: IP addresses use hierarchy to scale routing
Postal envelopes should show clearly delineated zip codes.
Q: How to identify the prefix from a 32-bit IP address?
  Two methods:
Old: Classful addressing. IP address itself is formatted to denote the IP prefix
New: Classless addressing (also called classless inter-domain routing, or CIDR).
  Each router independently identifies prefix from IP
NJ

## Slide 13: Classless IPv4 addressing (CIDR)

## Slide 14: Classless IPv4 addressing
Also called classless inter-domain routing (CIDR)
Key idea: Network component of the address (ie: prefix) can have any length (usually from 8—32)
Address format: a.b.c.d/x, where x is the prefix length
  Customary to use 0s for all suffix bits
11001000 00010111 00010000 00000000
network
part
host
part
200.23.16.0/23

## Slide 15: CIDR
An ISP can obtain a block of addresses and partition this further to its customers
Say an ISP has 200.8.0.0/16 address (65K addresses).
The ISP has customer who needs only 64 addresses starting from 200.8.4.128
Then that block can be specified as 200.8.4.128/26
200.8.4.128/26 is “inside” 200.8.0.0/16
200.8.0.0/16
200.8.4.128/26
200.8.0.0
200.8.0.1
200.8.1.0
…
200.8.1.1
…
200.8.255.255
https://www.internetsociety.org/resources/deploy360/2015/short-guide-ip-addressing/

## Slide 16: Netmask (or subnet mask)
An alternative to denote the IP prefix length of an organization
32 bits: a 1-bit denotes a prefix bit position. 0 denotes host bit.
11001000 00010111 00010000 00000000
network
part
host
part
200.23.16.0/23
11111111 11111111 11111110 00000000
network part of mask
host part of mask
Netmask: 255.255.254.0

## Slide 17: Detecting addresses from same network
Given IP addresses A and B, and netmask M.
1. Compute logical AND (A & M).
2. Compute logical AND (B & M).
3. If (A & M) == (B & M) then A and B are
on the same network.
Ex: A = 165.230.82.52, B = 165.230.24.93, M = 255.255.128.0
A and B are in the same network according to the netmask
A & M == B & M == 165.230.0.0

## Slide 18: Finding your own IP address(es)
The old way (still works today on Mac and Linux):
  ifconfig –a
The new way using “iproute2” tools on Linux:
  ip link
  ip addr
What else do you see in these outputs?

## Slide 19: Next we’ll talk about routers
Access routers
Core router
Data center top-of-rack switch

## Slide 20: What’s inside a router?

## Slide 21: Router architecture overview
high-speed
switching
fabric
route
processor
router input ports
router output ports
Control plane
Data plane
Review: Forwarding function: move packets from one input port to another.
Review: assuming distributed routing, routing function: decide which ports packets need to exit

## Slide 22: Different and evolving designs
There are different kinds of routers, with their own designs
  Access routers (e.g., home WiFi), chassis/core routers, top-of-rack switches
Router designs have also evolved significantly over time
For simplicity and concreteness, we will learn about one high-speed router design from the early 2000s.
Called the MGR (multi-gigabit router). It could support an aggregate rate of 50 Gbit/s (1 G = 109)
  Today’s single-chip routers can support aggregate rates of ~10 Tbit/s (1 T = 1012)

## Slide 23: Input port functions
Line termination: receives physical (analog) signals and turns them into digital signals
Rate of link connecting to a single port termed line speed or line rate (modern routers: 100+ Gbit/s)
Link layer: performs medium access control functions (e.g., Ethernet)
Line
Term
Link
Layer
/ MAC
(receive)
Route
lookup
switching
fabric
…
…
Switching fabric
Input port
Input port
Input port
Output port
Output port
Output port
Per-output
Queues

## Slide 24: Input port functions
Route lookup: high-speed lookup of which output port the packet is destined to
Goal: must complete this processing at the line rate
Queueing: packets may wait in per-output-port queues if packets are arriving too fast for the switching fabric to send them to the output port
Line
Term
Link
Layer
/ MAC
(receive)
Route
lookup
switching
fabric
…
…
Switching fabric
Input port
Input port
Input port
Output port
Output port
Output port
Per-output
Queues

## Slide 25: Route lookups
Packet forwarding in the Internet is based on the destination IP address on the packet.
Example: if dst IP on packet is 65.45.145.34, it matches the forwarding table prefix 65.0.0.0/8.
The packet is forwarded out port 3.
Example 2: what about dst IP 128.9.5.6?
Line
Term
Link
Layer
Route
lookup
Per-output
Queues
Outgoing Port
Dst-network
Port
Forwarding Table
Route Lookup Data Structure
65.0.0.0/8
128.9.0.0/16
149.12.0.0/19
3
1
7
Parse
Transport
Network
Link layer
Extract destination IP address

## Slide 26: Route lookups
Number of entries in the forwarding table matters.
Fitting into router memory
Designing hardware and software for fast lookups
Line
Term
Link
Layer
Route
lookup
Per-output
Queues
Outgoing Port
Dst-network
Port
Forwarding Table
Route Lookup Data Structure
65.0.0.0/8
128.9.0.0/16
149.12.0.0/19
3
1
7
Parse
Transport
Network
Link layer
Extract destination IP address

## Slide 27: Route lookups
Recall: IP addresses can be aggregated based on shared prefixes.
The number of table entries in a router is proportional to the number of prefixes, NOT the number of endpoints.
Today: ~ 1 million prefixes.
Line
Term
Link
Layer
Route
lookup
Per-output
Queues
Outgoing Port
Dst-network
Port
Forwarding Table
Route Lookup Data Structure
65.0.0.0/8
128.9.0.0/16
149.12.0.0/19
3
1
7
Parse
Transport
Network
Link layer
Extract destination IP address

## Slide 28: Route lookups
Destination-IP-based forwarding has consequences.
Forwarding behavior is independent of the source: legitimate source vs. malicious attack traffic
Forwarding behavior is independent of the application: web traffic vs. file download vs. video
IP-based packet processing is “baked into” router hardware: evolving the IP protocol faces tall deployment hurdles
Line
Term
Link
Layer
Route
lookup
Per-output
Queues
Outgoing Port
Dst-network
Port
Forwarding Table
Route Lookup Data Structure
65.0.0.0/8
128.9.0.0/16
149.12.0.0/19
3
1
7
Parse
Transport
Network
Link layer
Extract destination IP address

## Slide 29: Output port functions
Components in reverse order of those in the input port
This is where most routers have the bulk of their packet buffers
  Recall discussions regarding router buffers from transport
MGR uses per-port output buffers, but modern routers have shared memory buffers
  More efficient use of memory under varying demands
Line
Termination
Link
Layer
/ MAC
(transmit)
Queues
…
…
Switching fabric
Input port
Input port
Input port
Output port
Output port
Output port
Switching
fabric
To output link

## Slide 30: Output port functions
Two important policy decisions
Scheduling: which among the waiting packets gets to be transmitted out the link?
  Ex: First-In-First-Out (FIFO)
Buffer management: which among the packets arriving from the fabric get space in the packet buffer?
  Ex: Tail drop: later packets dropped first
Line
Termination
Link
Layer
/ MAC
(transmit)
Queues
…
…
Switching fabric
Input port
Input port
Input port
Output port
Output port
Output port
Switching
fabric
To output link

## Slide 31: Fabrics: Types
…
…
Switching fabric
Input port
Input port
Input port
Output port
Output port
Output port
Input port writes packets into shared memory.
Output port reads the packet when output link ready to transmit.
Single shared channel to move data from input to output port.
Easy to build buses; technology is quite mature.
Each input port has a physical data path to every output port.
Switch at the cross-over points turns on to connect pairs of ports.
Fabric goal: Ferry as many packets as possible from input to output ports as quickly as possible.

## Slide 32: Fabrics: Types
…
…
Switching fabric
Input port
Input port
Input port
Output port
Output port
Output port
Modern high-speed routers use highly optimized shared-memory-based interconnects.
Crossbars can get expensive as the number of ports grows (N2 connections for N ports)
MGR uses a crossbar and schedules (in,out) port pairs.

## Slide 33: Nonblocking fabrics
High-speed switching fabrics designed to be nonblocking:
  If an output port is “available”, an input port can always transmit to it without being blocked by the switching fabric itself
  Nontrivial to achieve
Crossbars are nonblocking by design
Shared memory can be designed to be nonblocking if the memory access is fast enough
…
…
Switching fabric
Input port
Input port
Input port
Output port
Output port
Output port

## Slide 34: Nonblocking fabrics
With a nonblocking fabric, queues aren’t formed due to the switching fabric.
  With a nonblocking fabric, there are no queues due to inefficiencies at the input port or the switching fabric
Queues only form due to contention for the output port
  Fundamental, unavoidable, given the route
…
…
Switching fabric
Input port
Input port
Input port
Output port
Output port
Output port

## Slide 35: Nonblocking fabrics
With a nonblocking fabric, queues aren’t formed due to the switching fabric.
  With a nonblocking fabric, there are no queues due to inefficiencies at the input port or the switching fabric
Queues only form due to contention for the output port
  Fundamental, unavoidable, given the route
Typically, these queues form on the output side
  But can also “backpressure” to the input side if there is high contention for the output port
  i.e.: can’t move pkts to output Qs since buffers full, so buffer @ input
…
…
Switching fabric
Input port
Input port
Input port
Output port
Output port
Output port

## Slide 36: Control (plane) processor
A general-purpose processor that “programs” the data plane:
  Forwarding table
  Scheduling and buffer management policy
Implements the routing algorithm by processing routing protocol messages
  Mechanism by which routers collectively solve the Internet routing problem
  More on this soon.
…
…
Switching fabric
Input port
Input port
Input port
Output port
Output port
Output port
Control Processor

## Slide 37
Routing
Algorithm
data
plane
control
plane
1
2
0111
values in arriving
packet header, i.e, destination IP address
3
Data plane
per-packet processing
(~ tens of nanoseconds)
Control plane
Traditional distributed routing: per route-change processing
(~ a few tens of seconds)
Router design: the bigger picture

## Slide 38: Longest Prefix Matching

## Slide 39: Review: Route lookup
Table lookup matches a packet against an IP prefix
  Ex: 65.12.45.2 matches 65.0.0.0/8
Prefixes are allocated to organizations by Internet registries
But organizations can reallocate a subset of their IP address allocation to other orgs
Outgoing Port
Dst-network
Port
Forwarding Table
Route Lookup Data Structure
65.0.0.0/8
128.9.0.0/16
149.12.0.0/19
3
1
7
Parse
Transport
Network
Link layer
Extract destination IP address

## Slide 40: Example of IP block reallocation
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
ISP A
Organization 1
Organization 8
Internet
Organization 2
200.23.20.0/23
Organization 3
.
.
.
.
.
.
ISP A owns the IP block 200.23.16.0/20.
Suppose ISP A reallocates a part of its IP block to orgs 1… 8
Dst IP Prefix | Output port
65.0.0.0/8 | 3
128.9.0.0/16 | 1
… | …
200.23.16.0/20 | 7 (towards A)
There is an announcement mechanism (BGP) by which ISP A can inform the rest of the Internet about the prefixes it owns.
It is enough to announce a coarse-grained prefix 200.23.16.0/20 rather than 8 separate sub-prefixes.
[BGP] Send me pkts destined to
200.23.16.0/20
Route Aggregation
Save forwarding table memory
Fewer routing protocol msgs

## Slide 41: Example of IP block reallocation
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
ISP A
Organization 1
Organization 8
Internet
Organization 2
200.23.20.0/23
Organization 3
.
.
.
.
.
.
ISP A owns the IP block 200.23.16.0/20.
Suppose ISP A reallocates a part of its IP block to orgs 1… 8
Dst IP Prefix | Output port
65.0.0.0/8 | 3
128.9.0.0/16 | 1
… | …
200.23.16.0/20 | 7 (towards A)
Now suppose one of these organizations adds another ISP for its Internet service and prefers using the new ISP.
Note: it’s possible for the organization to retain its assigned IP block.
[BGP] Send me pkts destined to
200.23.16.0/20

## Slide 42: Example of IP block reallocation
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
ISP A
Organization 1
Organization 8
Internet
Organization 2
200.23.20.0/23
Organization 3
.
.
.
.
.
.
ISP A owns the IP block 200.23.16.0/20.
Suppose ISP A reallocates a part of its IP block to orgs 1… 8
Dst IP Prefix | Output port
65.0.0.0/8 | 3
128.9.0.0/16 | 1
… | …
200.23.16.0/20 | 7 (towards A)
200.23.18.0/23
Organization 2
ISP B
[BGP] Announce 200.23.18.0/23
(besides other IP prefixes)
[BGP] Send me pkts destined to
200.23.16.0/20

## Slide 43: Example of IP block reallocation
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
ISP A
Organization 1
Organization 8
Internet
Organization 2
200.23.20.0/23
Organization 3
.
.
.
.
.
.
ISP A owns the IP block 200.23.16.0/20.
Suppose ISP A reallocates a part of its IP block to orgs 1… 8
Dst IP Prefix | Output port
65.0.0.0/8 | 3
128.9.0.0/16 | 1
200.23.18.0/23 | 4 (towards B)
200.23.16.0/20 | 7 (towards A)
200.23.18.0/23
Organization 2
ISP B
[BGP] Announce 200.23.18.0/23
(besides other IP prefixes)
[BGP] Send me pkts destined to
200.23.16.0/20

## Slide 44: A closer look at the forwarding table
200.23.18.0/23 is inside 200.23.16.0/20
A packet with destination IP address 200.23.18.xx is in both prefixes
  i.e., both entries match
Q: How should the router choose to forward the packet?
  The org prefers B, so should choose B
Dst IP Prefix | Output port
65.0.0.0/8 | 3
128.9.0.0/16 | 1
200.23.18.0/23 | 4 (towards B)
200.23.16.0/20 | 7 (towards A)
200.23.16.0/20

## Slide 45: Longest Prefix Matching (LPM)
Use the longest matching prefix, i.e., the most specific route, among all prefixes that match the packet.
Policy borne out of the Internet’s IP allocation model: prefixes and sub-prefixes are handed out
Internet routers use longest prefix matching.
  Very interesting algorithmic problems
  Challenges in designing efficient software and hardware data structures
Dst IP Prefix | Output port
65.0.0.0/8 | 3
128.9.0.0/16 | 1
200.23.18.0/23 | 4 (towards B)
200.23.16.0/20 | 7 (towards A)
200.23.16.0/20

## Slide 46
Internet routers perform longest-prefix matching on destination IP addresses of packets.

## Slide 47: Why is LPM prevalent?
An ISP (e.g., Verizon) has allocated a sub-prefix (or “subnet”) of a larger prefix that the ISP owns to an organization (e.g., Rutgers)
Further, the ISP announces the aggregated prefix to the Internet to save on number of forwarding table memory and number of announcements
The organization (e.g., Rutgers) is reachable over multiple paths (e.g., through another ISP like AT&T)
The organization has a preference to use one path over another, and expresses this by announcing the longer (more specific) prefix
Routers in the Internet must route based on the longer prefix
Rutgers
Verizon
AT&T
Agg. route
Specific route
(longer prefix)