## Slide 1: CS 352 Network: LPM, Protocols
Lecture 21
http://www.cs.rutgers.edu/~sn624/352-F22
Srinivas Narayana

## Slide 2: Quick recap of concepts
Net layer
high-speed
switching
fabric
route
processor
router input ports
router output ports
Blocking
Nonblocking
In nonblocking fabrics, queues form only due to contention for output port.
Output port contention is fundamental; unavoidable.
Scheduling and buffer management crucial.
Dst-network
Port
Forwarding Table
65.0.0.0/8
128.9.0.0/16
149.12.0.0/19
3
1
7
The Internet uses destination IP based forwarding.
Parse
Transport
Network
Link layer
Extract destination IP address
Lookup forwarding table

## Slide 3: Control (plane) processor
A general-purpose processor that “programs” the data plane:
  Forwarding table
  Scheduling and buffer management policy
Implements the routing algorithm by processing routing protocol messages
  Mechanism by which routers collectively solve the Internet routing problem
  More on this soon.
…
…
Switching fabric
Input port
Input port
Input port
Output port
Output port
Output port
Control Processor

## Slide 4
Routing
Algorithm
data
plane
control
plane
1
2
0111
values in arriving
packet header, i.e, destination IP address
3
Data plane
per-packet processing
(~ tens of nanoseconds)
Control plane
Traditional distributed routing: per route-change processing
(~ a few tens of seconds)
Router design: the bigger picture

## Slide 5: Longest Prefix Matching

## Slide 6: Review: Route lookup
Table lookup matches a packet against an IP prefix
  Ex: 65.12.45.2 matches 65.0.0.0/8
Prefixes are allocated to organizations by Internet registries
But organizations can reallocate a subset of their IP address allocation to other orgs
Outgoing Port
Dst-network
Port
Forwarding Table
Route Lookup Data Structure
65.0.0.0/8
128.9.0.0/16
149.12.0.0/19
3
1
7
Parse
Transport
Network
Link layer
Extract destination IP address

## Slide 7: Example of IP block reallocation
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
ISP A
Organization 1
Organization 8
Internet
Organization 2
200.23.20.0/23
Organization 3
.
.
.
.
.
.
ISP A owns the IP block 200.23.16.0/20.
Suppose ISP A reallocates a part of its IP block to orgs 1… 8
Dst IP Prefix | Output port
65.0.0.0/8 | 3
128.9.0.0/16 | 1
… | …
200.23.16.0/20 | 7 (towards A)
There is an announcement mechanism (BGP) by which ISP A can inform the rest of the Internet about the prefixes it owns.
It is enough to announce a coarse-grained prefix 200.23.16.0/20 rather than 8 separate sub-prefixes.
[BGP] Send me pkts destined to
200.23.16.0/20
Route Aggregation
Save forwarding table memory
Fewer routing protocol msgs

## Slide 8: Example of IP block reallocation
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
ISP A
Organization 1
Organization 8
Internet
Organization 2
200.23.20.0/23
Organization 3
.
.
.
.
.
.
ISP A owns the IP block 200.23.16.0/20.
Suppose ISP A reallocates a part of its IP block to orgs 1… 8
Dst IP Prefix | Output port
65.0.0.0/8 | 3
128.9.0.0/16 | 1
… | …
200.23.16.0/20 | 7 (towards A)
Now suppose one of these organizations adds another ISP for its Internet service and prefers using the new ISP.
Note: it’s possible for the organization to retain its assigned IP block.
[BGP] Send me pkts destined to
200.23.16.0/20

## Slide 9: Example of IP block reallocation
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
ISP A
Organization 1
Organization 8
Internet
Organization 2
200.23.20.0/23
Organization 3
.
.
.
.
.
.
ISP A owns the IP block 200.23.16.0/20.
Suppose ISP A reallocates a part of its IP block to orgs 1… 8
Dst IP Prefix | Output port
65.0.0.0/8 | 3
128.9.0.0/16 | 1
… | …
200.23.16.0/20 | 7 (towards A)
200.23.18.0/23
Organization 2
ISP B
[BGP] Announce 200.23.18.0/23
(besides other IP prefixes)
[BGP] Send me pkts destined to
200.23.16.0/20

## Slide 10: Example of IP block reallocation
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
ISP A
Organization 1
Organization 8
Internet
Organization 2
200.23.20.0/23
Organization 3
.
.
.
.
.
.
ISP A owns the IP block 200.23.16.0/20.
Suppose ISP A reallocates a part of its IP block to orgs 1… 8
Dst IP Prefix | Output port
65.0.0.0/8 | 3
128.9.0.0/16 | 1
200.23.18.0/23 | 4 (towards B)
200.23.16.0/20 | 7 (towards A)
200.23.18.0/23
Organization 2
ISP B
[BGP] Announce 200.23.18.0/23
(besides other IP prefixes)
[BGP] Send me pkts destined to
200.23.16.0/20

## Slide 11: A closer look at the forwarding table
200.23.18.0/23 is inside 200.23.16.0/20
A packet with destination IP address 200.23.18.xx is in both prefixes
  i.e., both entries match
Q: How should the router choose to forward the packet?
  The org prefers B, so should choose B
Dst IP Prefix | Output port
65.0.0.0/8 | 3
128.9.0.0/16 | 1
200.23.18.0/23 | 4 (towards B)
200.23.16.0/20 | 7 (towards A)
200.23.16.0/20
The Internet uses a policy to prioritize: Longest Prefix Matching

## Slide 12: Longest Prefix Matching (LPM)
Use the longest matching prefix, i.e., the most specific route, among all prefixes that match the packet.
Policy borne out of the Internet’s IP allocation model: prefixes and sub-prefixes are handed out
Internet routers use longest prefix matching.
  Very interesting algorithmic problems
  Challenges in designing efficient software and hardware data structures
Dst IP Prefix | Output port
65.0.0.0/8 | 3
128.9.0.0/16 | 1
200.23.18.0/23 | 4 (towards B)
200.23.16.0/20 | 7 (towards A)
200.23.16.0/20

## Slide 13
Internet routers perform longest-prefix matching on destination IP addresses of packets.

## Slide 14: Why is LPM prevalent?
An ISP (e.g., Verizon) has allocated a sub-prefix (or “subnet”) of a larger prefix that the ISP owns to an organization (e.g., Rutgers)
Further, the ISP announces the aggregated prefix to the Internet to save on number of forwarding table memory and number of announcements
The organization (e.g., Rutgers) is reachable over multiple paths (e.g., through another ISP like AT&T)
The organization has a preference to use one path over another, and expresses this by announcing the longer (more specific) prefix
Routers in the Internet must route based on the longer prefix
Rutgers
Verizon
AT&T
Agg. route
Specific route
(longer prefix)

## Slide 15: IPv4 Datagram Format

## Slide 16
ver
length
32 bits
data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
32-bit source IP address
IP protocol version
number
header length
(bytes)
max number
remaining hops
(decremented at
each router)
for
fragmentation/
reassembly
total datagram
length (bytes)
upper layer protocol to deliver payload to, e.g., TCP, UDP
hdr
len
type of
service
Bits for
traffic differentiation
e.g., audio, web, bulk
(more on this later)
flags
fragment
offset
upper
protocol
32-bit destination IP address
Options (if any)
E.g. timestamp,
record the route
taken, specify
list of routers
to visit (“source routing”)
How much header overhead?
Suppose 20 bytes of TCP
20 bytes of IP
= 40 bytes
Transport
Network
Link layer

## Slide 17: Rest of this lecture
Discuss support protocols and mechanisms for the network layer
  Protocols: DHCP, ICMP, ARP, IPv6, …
  Mechanisms: NAT
Some of these protocols use an IP header underneath their own header (ICMP) or replace the IP header with their own (ARP)
  But these shouldn’t be construed as transport/network protocols
  They are fundamental to supporting IP/network layer functionality
  More appropriately discussed as support protocols for the network layer

## Slide 18
The network layer is all about reachability.
Every protocol we’ll see solves a sub-problem.
How does an endpoint get an address?
DHCP
How does an endpoint talk to another within the same network?
ARP
How does an endpoint talk to another outside its network?
Routing protocols
OSPF, RIP, BGP
Gateways
NAT & IPv6
Debugging?
ICMP

## Slide 19: Internet Control Message Protocol (ICMP)

## Slide 20: Internet Control Message Protocol
A protocol for troubleshooting and diagnostics
Works over IP: unreliable delivery of packets
Some functions of ICMP:
  Determine reachability and network errors
  Specify that packets have been in the network for too long

## Slide 21: ICMP message format (informal)
IP header
ICMP header
Message type, Code, Checksum,
ICMP data
https://en.wikipedia.org/wiki/Internet_Control_Message_Protocol#Control_messages

## Slide 22: Specific uses of ICMP
Echo request reply
  Check remotely if an endpoint is alive and connected
  Without running an app remotely or controlling that endpoint
An unreachable destination
  Invalid address and/or port
Knowing if packet’s IP time-to-live expired
  Example, due to routing loops
Look at two tools built using ICMP: ping and traceroute

## Slide 23: Ping
Uses ICMP echo request (type=8, code=0) and reply (type=0, code=0)
Source sends ICMP echo request message to dst address
Destination network stack replies with an ICMP echo reply message
Source can calculate round trip time (RTT) of packets
If no echo reply comes back, then the destination is unreachable
Don’t need to have a server program running on the other side
  In general, the remote endpoint can be completely outside your control

## Slide 24: Ping
Time
Echo
request
Echo reply
A
B
R1
R2
R3
Ping time
A small demo…

## Slide 25: Traceroute
A tool that can record the router-level path taken by packets
A clever use of the IP time-to-live (TTL) field
In general, when a router receives an IP packet, it decrements the TTL field on the packet
  A failsafe mechanism to ensure packets don’t keep taking up network resources for too long
If a router receives a packet with TTL=0, it sends an ICMP time exceeded message (type=11, code=0) to the source endpoint

## Slide 26: Traceroute
Traceroute sends multiple packets to a destination endpoint
But it progressively increases the TTL on those packets: 1, 2, ...
Every time a time exceeded message is received, record the router’s IP address
Process repeated until the destination endpoint is reached
If the packet reaches the destination endpoint (i.e.: TTL is high enough), then the endpoint sends a port unreachable message (type=3, code=3)

## Slide 27: Traceroute
Time
TTL=1, dest = B, dstport = invalid
A
B
R1
R2
R3
A small demo…
Time exceeded
Source: R1
TTL = 2
TE(R2)
Port un- reachable
Source: B
Similarly, capture IP addresses of routers at distance 3, 4, …
Have full router-level path until destination

## Slide 28: Summary of ICMP
A protocol for network diagnostics and troubleshooting
Two useful tools: ping and traceroute
Ping: test connectivity to a machine totally outside your control
  Use ICMP echo request and reply
Traceroute: determine router-level path to a remote endpoint
  A smart use of the TTL field in the IP header

## Slide 29: Network Address Translation (NAT)

## Slide 30: Background: The Internet’s growing pains
Networks had incompatible addressing
  IPv4 versus other network-layer protocols (X.25)
  Routable address ranges different across networks
Entire networks were changing their Internet Service Providers
  ISPs don’t want to route directly to internal endpoints, just to the gateway
IPv4 address exhaustion
  Insufficient large IP blocks even for large networks
  Rutgers (AS46) has > 130,000 publicly routable IP addresses
  IIT Madras (a well-known public university in India, AS141340) has 512
  (Source: ipinfo.io)

## Slide 31: Network Address Translation
When a router modifies fields in an IP packet to:
Enable communication across networks with different (network-layer) addressing formats and address ranges
Allow a network to change its connectivity to the Internet en masse by modifying the source IP to a (publicly-visible) gateway IP address
Masquerade as an entire network of endpoints using (say) one publicly visible IP address
  Effect: use fewer IP addresses for more endpoints!
We’ll see a standard design: “Network address and port translation” (NAPT)

## Slide 32: Typical NAT setup (NAPT)
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
138.76.29.7
local network
10.0.0/24
rest of
the Internet
The gateway’s IP, 138.76.29.7 is publicly visible
The local endpoint IP addresses in 10.0.0/24 are private
All datagrams leaving local network have the same source IP as the gateway
Gateway router

## Slide 33: Typical NAT setup (NAPT)
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
local network
10.0.0/24
rest of
the Internet
That is, for the rest of the Internet, the gateway masquerades as a single endpoint representing (hiding) all the private endpoints.
The entire network just needs one (or a few) public IP addresses.
Gateway router
138.76.29.7

## Slide 34: Typical NAT setup (NAPT)
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
local network
10.0.0/24
rest of
the Internet
The NAT gateway router accomplishes this by using a different transport port for each distinct (transport-level) conversation between the local network and the Internet.
Gateway router
138.76.29.7

## Slide 35: Typical NAT setup (NAPT)
10.0.0.1
10.0.0.2
10.0.0.3
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
1: host 10.0.0.1
sends datagram to
an external host,
128.119.40.186, at port 80
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router
changes datagram
src addr, port from
10.0.0.1, 3345 to
138.76.29.7, 5001,
Updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: Reply arrives to
dst addr, port
138.76.29.7, 5001
4: NAT gateway
changes datagram
dest addr, port from
138.76.29.7, 5001 to
10.0.0.1, 3345
Translation table
Internet-side Local side
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
4: Map back
138.76.29.7

## Slide 36: Features of IP-masquerading NAT
Use one or a few public IPs: You don’t need a lot of addresses from your ISP
Change addresses of devices inside the local network freely, without notifying the rest of the Internet
Change the public IP address freely independent of network-local endpoints
Devices inside the local network are not publicly visible, routable, or accessible
Most IP masquerading NATs block incoming connections originating from the Internet
  Only way to communicate is if the internal host initiates the conversation

## Slide 37: If you’re home, you’re likely behind NAT
Most access routers (e.g., your home WiFi router) implement network address translation
You can check this by comparing your local address (visible from ifconfig) and your externally-visible IP address (e.g., type “what’s my IP address?” on your browser search bar)

## Slide 38: If you’re home, you’re likely behind NAT

## Slide 39: Limitations of IP-masquerading NATs
Connection limit due to 16-bit port-number field
  ~64K total simultaneous connections with a single public IP address
NAT can be controversial
  “Routers should only manipulate headers up to the network layer, not modify headers at the transport layer!”
Application developers must take NAT into account
  e.g., peer-to-peer applications like Skype
Internet “purists”: instead, solve address shortage with IPv6
  32-bit IP addresses are just not enough
  Esp. with more devices (your watch, your fridge, …) coming online