## Slide 1: CS 352 Network: ICMP, NAT, Routing
Lecture 22
http://www.cs.rutgers.edu/~sn624/352-F22
Srinivas Narayana

## Slide 2: Review
IPv4 datagram
Dst IP Prefix | Output port
65.0.0.0/8 | 3
128.9.0.0/16 | 1
200.23.18.0/23 | 4 (towards B)
200.23.16.0/20 | 7 (towards A)
200.23.16.0/20
Longest Prefix Matching
Net layer
Echo
request
A
Time
B
…
Echo
reply
Ping time
…
ICMP echo request and reply.
ping

## Slide 3: Traceroute
A tool that can record the router-level path taken by packets
A clever use of the IP time-to-live (TTL) field
In general, when a router receives an IP packet, it decrements the TTL field on the packet
  A failsafe mechanism to ensure packets don’t keep taking up network resources for too long
If a router receives a packet with TTL=0, it sends an ICMP time exceeded message (type=11, code=0) to the source endpoint

## Slide 4: Traceroute
Traceroute sends multiple packets to a destination endpoint
But it progressively increases the TTL on those packets: 1, 2, ...
Every time a time exceeded message is received, record the router’s IP address
Process repeated until the destination endpoint is reached
If the packet reaches the destination endpoint (i.e.: TTL is high enough), then the endpoint sends a port unreachable message (type=3, code=3)

## Slide 5: Traceroute
Time
TTL=1, dest = B, dstport = invalid
A
B
R1
R2
R3
A small demo…
Time exceeded
Source: R1
TTL = 2
TE(R2)
Port un- reachable
Source: B
Similarly, capture IP addresses of routers at distance 3, 4, …
Have full router-level path until destination

## Slide 6: Summary of ICMP
A protocol for network diagnostics and troubleshooting
Two useful tools: ping and traceroute
Ping: test connectivity to a machine totally outside your control
  Use ICMP echo request and reply
Traceroute: determine router-level path to a remote endpoint
  A smart use of the TTL field in the IP header

## Slide 7: Network Address Translation (NAT)

## Slide 8: Background: The Internet’s growing pains
Networks had incompatible addressing
  IPv4 versus other network-layer protocols (X.25)
  Routable address ranges different across networks
Entire networks were changing their Internet Service Providers
  ISPs don’t want to route directly to internal endpoints
IPv4 address exhaustion
  Insufficient large IP blocks even for large networks
  Rutgers (AS46) has > 130,000 publicly routable IP addresses
  IIT Madras (a well-known public university in India, AS141340) has 512
  (Source: ipinfo.io)

## Slide 9: Network Address Translation
When a router modifies fields in an IP packet to:
Enable communication across networks with different (network-layer) addressing formats and address ranges
Allow a network to change its connectivity to the Internet en masse by modifying the source IP to a (publicly-visible) gateway IP address
Masquerade as an entire network of endpoints using (say) one publicly visible IP address
  Effect: use fewer IP addresses for more endpoints!
We’ll see a standard design: “Network address and port translation” (NAPT, RFC 2663)

## Slide 10: Typical NAT setup (NAPT)
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
138.76.29.7
local network
10.0.0/24
rest of
the Internet
The gateway’s IP, 138.76.29.7 is publicly visible
The local endpoint IP addresses in 10.0.0/24 are private
All datagrams leaving local network have the same source IP as the gateway
Gateway router

## Slide 11: Typical NAT setup (NAPT)
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
local network
10.0.0/24
rest of
the Internet
That is, for the rest of the Internet, the gateway masquerades as a single endpoint representing (hiding) all the private endpoints.
The entire network just needs one (or a few) public IP addresses.
Gateway router
138.76.29.7

## Slide 12: Typical NAT setup (NAPT)
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
local network
10.0.0/24
rest of
the Internet
The NAT gateway router accomplishes this by using a different transport port for each distinct (transport-level) conversation between the local network and the Internet.
Gateway router
138.76.29.7

## Slide 13: Typical NAT setup (NAPT)
10.0.0.1
10.0.0.2
10.0.0.3
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
1: host 10.0.0.1
sends datagram to
an external host,
128.119.40.186, at port 80
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router
changes datagram
src addr, port from
10.0.0.1, 3345 to
138.76.29.7, 5001,
Updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: Reply arrives to
dst addr, port
138.76.29.7, 5001
4: NAT gateway
changes datagram
dest addr, port from
138.76.29.7, 5001 to
10.0.0.1, 3345
Translation table
Internet-side Local side
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
4: Map back
138.76.29.7

## Slide 14: Features of IP-masquerading NAT
Use one or a few public IPs: You don’t need a lot of addresses from your ISP
Change addresses of devices inside the local network freely, without notifying the rest of the Internet
Change the public IP address freely independent of network-local endpoints
Devices inside the local network are not publicly visible, routable, or accessible
Most IP masquerading NATs block incoming connections originating from the Internet
  Only way to communicate is if the internal host initiates the conversation

## Slide 15: If you’re home, you’re likely behind NAT
Most access routers (e.g., your home WiFi router) implement network address translation
You can check this by comparing your local address (visible from ifconfig) and your externally-visible IP address (e.g., type “what’s my IP address?” on your browser search bar)

## Slide 16: If you’re home, you’re likely behind NAT

## Slide 17: On public cloud, you’re behind NAT
VM
Physical Machine
Each VM believes it has its own IP address.
VM
Each VM believes it has its own IP address.
Physical Machine
Physical
addresses used
NAT
NAT

## Slide 18: Limitations of IP-masquerading NATs
Connection limit due to 16-bit port-number field
  ~64K total simultaneous connections with a single public IP address
NAT can be controversial
  “Routers should only manipulate headers up to the network layer, not modify headers at the transport layer!”
Application developers must take NAT into account
  e.g., peer-to-peer applications like Skype
Internet “purists”: instead, solve address shortage with IPv6
  32-bit IP addresses are just not enough
  Esp. with more devices (your watch, your fridge, …) coming online

## Slide 19: Routing Protocols

## Slide 20
The network layer is all about reachability.
Every protocol below solves a sub-problem.
DHCP
How does an endpoint get an address?
How does an endpoint talk to another within the same network?
ARP
How does an endpoint talk to another outside its network?
Routing protocols
OSPF, RIP, BGP
Gateways
NAT
Debugging
ICMP
ping
traceroute
Net layer
IPv6

## Slide 21: Review: Key network-layer functions
Forwarding (data plane): move packets from router’s input to appropriate router output
Routing (control plane): determine route taken by packets from source to destination
Analogy: taking a road trip
Forwarding: process of getting through single interchange
Routing: process of planning trip from source to destination
network
layer
runs
everywhere

## Slide 22
How would one design a “Google Maps”
to navigate the Internet?
Routing is a fundamental problem in networking.

## Slide 23: Goals of Routing Protocols #1
Determine good paths from source to destination
“Good” = least cost
  Least propagation delay
  Least cost per unit bandwidth (e.g., $ per Gbit/s)
  Least congested (workload-driven)
“Path” = a sequence of router ports (links)

## Slide 24: Goals of Routing Protocols #2
Make networks resilient to failures
Routers & links can fail without taking down the entire network
Entire subsets can be unreachable; rest still reachable
Hence, the protocol must be distributed

## Slide 25
Routing
Algorithm
data
plane
control
plane
1
2
0111
values in arriving
packet header,
i.e, destination IP address
3
Data plane
per-packet processing, moving packet from input port to output port
Distributed control plane: Components in every router interact with other components to produce a routing outcome.
Per-router control plane
Q1. What info exchanged?
Q2. What computation?
Routing protocol

## Slide 26: The graph abstraction
Routing algorithms work over an abstract representation of a network: the graph abstraction
Each router is a node in a graph
Each link is an edge in the graph
Edges have weights (also called link metrics). Set by netadmin
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
Ex: Rutgers campus
u: Computer Science
v: School of Engineering
…

## Slide 27: The graph abstraction
Routing algorithms work over an abstract representation of a network: the graph abstraction
G = (N, E)
N = {u, v, w, x, y, z}
E = { (u,v), (u,x), (v,x), (v,w), (x,w), (x,y), (w,y), (w,z), (y,z) }
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
Ex: Rutgers campus
u: Computer Science
v: School of Engineering
…

## Slide 28: The graph abstraction
Cost of an edge: c(x, y)
  Examples: c(u, v) = 2, c(u, w) = 5
Cost of a path = sum of edge costs
  c(path x  w  y  z) = 3 + 1 + 2 = 6
Outcome of routing: each node should determine the least cost path to every other node
Q1: What information should nodes exchange with each other to enable this computation?
Q2: What algorithm should each node run to compute the least cost path to every node?
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5

## Slide 29: Coming up next
Routing protocols
Link state
protocols
Distance vector protocols
Each router has complete information of the graph
Messages exchanged by flooding all over the network
Communication expensive, but complete
Each router only maintains distances & next hop to others
Messages are exchanged over each link and stay within the link
Communication cheap, but incomplete

## Slide 30: Link State Protocols

## Slide 31: Link state protocol
Each router knows the state of all the links and routers in the network
Every router performs an independent computation on globally shared knowledge of network’s complete graph representation
Distance vector protocols
Routing protocols
Link state
protocols

## Slide 32: Q1: Information exchange
Link state flooding: the process by which neighborhood information of each network router is transmitted to all other routers
Each router sends a link state advertisement (LSA) to each of its neighbors
LSA contains the router ID, the IP prefix owned by the router, the router’s neighbors, and link cost to those neighbors
Upon receiving an LSA, a router forwards it to each of its neighbors: flooding
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5

## Slide 33: Q1: Information exchange
Eventually, the entire network receives LSAs originated by each router
LSAs put into a link state database
LSAs occur periodically and whenever the graph changes
  Example: if a link fails
  Example: if a new link or router is added
The routing algorithm running at each router can use the entire network’s graph to compute least cost paths
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5

## Slide 34: Q2: The algorithm
Dijkstra’s algorithm
Given a network graph, the algorithm computes the least cost paths from one node (source) to all other nodes
This can then be used to compute the forwarding table at that node
Iterative algorithm: maintain estimates of least costs to reach every other node. After k iterations, each node definitively knows the least cost path to k destinations
Notation:
c(x,y): link cost from node x to y; = ∞ if not direct neighbors
D(v): current estimate of cost of path from source to destination v
p(v): (predecessor node) the last node before v on the path from source to v
N': set of nodes whose least cost path is definitively known

## Slide 35: Dijsktra’s Algorithm
1 Initialization:
2 N' = {u}
3 for all nodes v
4 if v adjacent to u
5 then D(v) = c(u,v)
6 else D(v) = ∞
7
8 Loop
9 find w not in N' such that D(w) is a minimum
10 add w to N'
11 update D(v) for all v adjacent to w and not in N' :
12 D(v) = min( D(v), D(w) + c(w,v) )
13 /* new cost to v is either old cost to v or known
14 shortest path cost to w plus cost from w to v */
15 until all nodes in N'
Initial estimates of distances are just the link costs of neighbors.
Least cost node among all estimates. This cost cannot decrease further.
Relaxation

## Slide 36: Visualization
v
w
u
N’
nodes whose least cost paths from u are definitively known
v’
v’’
N \ N’
Nodes with estimated least path costs, not definitively known to be smallest possible
min cost in N \ N’
D(w)
c(w, v)
D(v)
W should move to N’.
Relaxation: for each v in N \ N’, is the cost of the path via w smaller than known least cost path to v?
If so, update D(v)
Predecessor of v is w.
Cost of path via w: D(w) + c(w,v)
Cost of known best path: D(v)

## Slide 37: Dijkstra’s algorithm: example
Step
0
1
2
3
4
5
N'
u
ux
uxy
uxyv
uxyvw
uxyvwz
D(v),p(v)
2,u
2,u
2,u
D(w),p(w)
5,u
4,x
3,y
3,y
D(x),p(x)
1,u
D(y),p(y)
∞
2,x
D(z),p(z)
∞
∞
4,y
4,y
4,y
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5

## Slide 38: Constructing the forwarding table
To find the router port to use for a given destination (router), find the predecessor of the node iteratively until reaching an immediate neighbor of the source u
The port connecting u to this neighbor is the output port for this destination

## Slide 39: Constructing the forwarding table
Suppose we want forwarding entry for z.
D(v),p(v)
2,u
D(w),p(w)
3,y
D(x),p(x)
1,u
D(y),p(y)
2,x
D(z),p(z)
4,y
z: p(z) = y
y: p(y) = x
x: p(x) = u
x is an immediate
neighbor of u
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
z
(u,x)
destination
link
Forwarding table at u:

## Slide 40: Summary of link state protocols
Each router announces link state to the entire network using flooding
Each node independently computes least cost paths to every other node using the full network graph
Dijkstra’s algorithm can efficiently compute these best paths
  Easy to populate the forwarding table from predecessor information computed during the algorithm