## Slide 1: Revisiting RowHammer An Experimental Analysis of Modern Devices and Mitigation Techniques
Jeremie S. Kim Minesh Patel
A. Giray Yağlıkçı Hasan Hassan
Roknoddin Azizi Lois Orosa Onur Mutlu
Notes: Hello, my name is Jeremie Kim and I will be presenting our work revisiting rowhammer: an experimental analysis of modern devices and mitigation techniques

## Slide 2: The RowHammer Vulnerability
Row 0
Row 1
Row 2
Row 3
Row 4
Repeatedly opening (activating) and closing (precharging)
a DRAM row causes RowHammer bit flips in nearby cells
Row 2
open
Row 1
Row 3
Row 2
closed
Row 2
open
Row 1
Row 3
Row 0
Row 4
Row 2
closed
Victim Row
Victim Row
Victim Row
Victim Row
Aggressor Row
Row 2
open
Row 2
closed
Aggressor Row
DRAM Chip
2/6
Notes: In order to access data from a DRAM row, say row 2, the memory controller must first open or activate the row [CLICK].
After all requests are serviced from row 2, the memory controller must close or precharge the row [CLICK] in order to begin accessing data from another row.
[BACK & FORTH] Due to an increase in cell-to-cell interference as a likely result of increased cell packing density, rapidly activating and precharging a DRAM row can result in bit flips in nearby rows [CLICK]
[FORTH & BACK] Continuing to access the same row results in even more failures in nearby rows. This phenomenon is known as RowHammer. [CLICK]
We refer to the rapidly accessed row as an aggressor row and the rows containing bit flips as victim rows.
========

## Slide 3: Motivation and Goal
  Denser DRAM chips are more vulnerable to RowHammer
  Three prior works [Kim+, ISCA’14], [Park+, MR’16], [Park+, MR’16], over the last six years provide RowHammer characterization data on real DRAM
  However, there is no comprehensive experimental study that demonstrates how vulnerability scales across DRAM types and technology node generations
  Unclear whether current mitigation mechanisms will remain viable for future DRAM chips that are likely to be more vulnerable to RowHammer
Goal:
  Experimentally demonstrate how vulnerable modern DRAM chips are to RowHammer and study how this vulnerability will scale going forward
  Study viability of existing mitigation mechanisms on more vulnerable chips
3/6
Notes: [CLICK] denser DRAM chips are more vulnerable to RowHammer
[CLICK] Three prior works provide RowHammer characterization data on real DRAM chips.
[CLICK] However, there is no comprehensive experimental study that demonstrates how the RowHammer vulnerability scales across DRAM types and technology node generations and as DRAM chips become more dense
[CLICK] Therefore it is hard to identify whether current mitigation mechanisms will remain viable for future DRAM chips that are likely to be more vulnerable to RowHammer
[CLICK] The goal of this work is to
[CLICK] First, experimentally demonstrate how vulnerable modern DRAM chips are to RowHammer and predict how this vulnerability will scale going forward and
[CLICK] Second, we want to study the viability of current mitigation mechanisms on more vulnerable chips.
=============

## Slide 4: Experimental Characterization
We examine 1580 total DRAM chips from 300 DRAM modules
Three major DRAM manufacturers {A, B, C}
Three DRAM types or standards {DDR3, DDR4, LPDDR4}
Two technology nodes per DRAM type {old/new, 1x/1y}
Key Takeaways
Chips of newer DRAM technology nodes are more vulnerable to RowHammer
  i.e., 69.2k to 22.4k in DDR3, 17.5k to 10k in DDR4, and 16.8k to 4.8k in LPDDR4 chips
There are chips today whose weakest cells fail after only 4800 hammers (i.e., 4800 accesses to two rows each)
Chips of newer DRAM technology nodes can exhibit RowHammer bit flips 1) in more rows and 2) farther away from the victim row.
4/6
Notes: [CLICK] We characterize over 1500 DRAM chips from 300 DRAM modules
[CLICK] spanning the three major DRAM manufacturers which we anonymize as A, B, and C
[CLICK] of three DRAM types or standards DDR3, DDR4, and LPDDR4.
[CLICK] We identify two technology nodes per DRAM type (old/new, 1x and 1y) , which we categorize based on manufacturing date, datasheet publication date, purchase date, and characterization results
[CLICK] From our experimental characterization, we make three key observations.
[CLICK] First, chips of newer DRAM technology nodes are more vulnerable to RowHammer
[CLICK] Second, there are chips today whose weakest cells fail after only 4800 hammers or 4800 accesses to two rows each.
[CLICK] Third, chips of newer DRAM technology nodes can exhibit RowHammer bit flips in more rows and farther away from the victim row
================

## Slide 5: Mitigation Mechanism Evaluation
105
104
103
102
HCfirst
DRAM’s Vulnerability to RowHammer
More Vulnerable
Less Vulnerable
Vulnerability Today
PARA
TWiCe-ideal
Ideal
Increased Refresh
MRLoc
ProHIT
TWiCe
We evaluate system performance impact on chips of varying degrees of vulnerability for
five state-of-the-art mitigation mechanisms:
  Increased Refresh Rate [Kim+, ISCA’14], PARA [Kim+, ISCA’14], ProHIT [Son+, DAC’17], MRLoc [You+, DAC’19], TWiCe [Lee+, ISCA’19]
one ideal refresh-based mitigation mechanism:
  Ideal
Available mechanisms mitigate RowHammer in worst chips today
with reasonable system performance (92%, 100%, 100%)
We need better solutions for future chips that are likely more vulnerable
Notes: [CLICK] We also evaluate the system performance impact when using different mitigation mechanisms on chips of varying degrees of vulnerability for
[CLICK] five state of the art mitigation mechanisms and
[CLICK] one ideal refresh-based mitigation mechanism in green.
[CLICK] we indicate, with the orange vertical line, the worst degree of RowHammer vulnerability that we observed across the modern DRAM chips that we characterized and
[CLICK] We find that available mitigation mechanisms can mitigate RowHammer in worst chips today with reasonable system performance overhead.
However, we need better solutions for future DRAM chips that are likely to be more vulnerable to RowHammer, as existing mitigation mechanisms either do not scale to support chips of very high degrees of RowHammer vulnerability or have significantly high performance overheads.

## Slide 6: Revisiting RowHammer An Experimental Analysis of Modern Devices and Mitigation Techniques
Jeremie S. Kim Minesh Patel
A. Giray Yağlıkçı Hasan Hassan
Roknoddin Azizi Lois Orosa Onur Mutlu
Notes: Thank you for your time and attention. I invite you to listen to our full talk and read our paper for more details.
=================================================
Thank you for your time and attention and I look forward to answering your questions in my session today at noon.