## Slide 1
3: Motivations
Reducing DRAM Latency via
Charge-Level-Aware Look-Ahead Partial Restoration
Yaohua Wang1,2 Arash Tavakkol1 Lois Orosa1,4 Saugata Ghose3 Nika Mansouri Ghiasi1
Minesh Patel1 Jeremie S. Kim1 Hasan Hassan1 Mohammad Sadrosadati1 Onur Mutlu1,3
1: Summary
DRAM latency is a major bottleneck:
Mainly consists of: activation and restoration
Partial restoration on soon-to-be refreshed cells can help to reduce restoration latency
Motivation:
The potential of partial restoration can be greatly improved when applied on soon-to-be-reactivated cells
We can trade-off restoration and activation latency reductions to maximize the overall benefit
Charge-level-aware look-ahead Partial restoration (CAL):
Accurately predict the next access-to-access interval
Carefully apply partial restoration according to the prediction and next scheduled refresh
Greatly improve overall performance and energy efficiency at low cost
2: Background and Key Ideas
DRAM subarray structure
(a) To compensate for the charge depletion and avoid data loss, DRAM fully restores the charge level of the cell during access; (b) Restore Truncation[Zhang+,HPCA 2016] partially restores the charge of soon-to-be-refreshed cell to a level, such that the amount of charge is just enough to ensure that the refresh operation can still correctly read the data; (c) CAL effectively enable partial restoration for both soon-to-be-refreshed and soon-to-be-reactivated cells, while still effectively exploiting the benefits of activation latency reduction
1
How to know the
next access-to-access interval?
Applying partial restoration on soon-to-be-reactivated DRAM cells can provide larger benefit
  A charge level aware partial restoration can trade a smaller tRCD reduction for a larger tRAS reduction.
2
4: Charge-Level-Aware Look-Ahead Partial Restoration
1. Uses the last access-to-access interval of a row to predict whether the row will be reactivated again soon
Key Mechanism
Tag
Timer Table
Insert
[PRE]
Lookup
[ACT][WRITE]
1
5
2
Hardware Structure
Reduced Timing Parameters
Three cases to reduce tRCD/tRAS/tWR according to the timer value (T):
T == 15: < 1ms since last restoration
11.2/16.1/6.8ns
0 < T < 15: 1-15ms since last restoration
13.75/19.4/8.4ns
T == 0: >15ms passed (or lookup miss)
Default parameters
5: Evaluation
Methodology
Simulator
  DRAM Simulator (Ramulator [Kim+, CAL’15])
    https://github.com/CMU-SAFARI/ramulator
Workloads
  20 single-core workloads
    SPEC CPU2006, TPC, BioBench
  20 multi-programmed 8-core workloads
    By randomly choosing from single-core workloads
Mechanism Parameters
  8-way cache-like set-associative timer table
  DDR4 timing tRCD/tRAS/tWR: 13.75/35/15ns
Mechanisms Evaluated
  Insertion: New items are inserted upon PRE command, potentially evicting other items, and issuing ACT and PRE commands
  Initialization: The timer value is initialized upon PRE command
  Update: The timer table performs an update every 1ms to record access intervals
  Lookup: Each ACT/WRITE incurs a lookup in the timer table to reduce timing parameters accordingly
Performance Improvement
CAL always outperforms the other mechanisms
By an average of 7.4%(14.7%) for single-core (8-core) workloads
System Energy Breakdown
On average, CAL reduces system energy by 10.1% and 18.9%
for memory intensive single-core and 8-core workloads
Area: 0.034mm2, 0.11% of 16MB LLC
Power: 0.202mW, 0.08% of 16MB LLC
CAL’s performance is robust across various configurations
  TC table size
  Page management policy
  Address mapping policy
Partial restoration level plays an important role, trading tRCD with tRAS reduction can provide opportunities for performance gain
CAL’s is still effective to high temperatures, where the refresh rate is increased
1
2
3
4
6: Hardware Overhead & Sensitivity Analysis
Two ciritial parts of DRAM access latency:
Activation: Sensing and amplifying the charge of cell (tRCD)
Restoration: Restoring the charge of cell after access (tRAS)
Evict
[PRE]
[ACT]
Self-update
Every 1ms
4
  CAL
  ChargeCache (CC) [Hassan+, HPCA’16]
  reduces tRCD and tRAS for highly-charged rows
  Restore Truncation (RT) [Xian+, HPCA16]
  reduces tRAS and tWR for soon-to-be-refreshed rows
  Combinations of activation and restoration latency reductions
  CCRT: a simple combination of CC and RT
  GreedyPR: similar to CAL, but unaware of future charge level
  Idealized CAL (IdealCAL)
High Level Operations
National University of
Defense Technology
University of
Campinas
2. Decides by how much the restoration latency should be reduced, based on the prediction and trade-off
Initialization
[PRE]
3
Timer
V
PR
Tag: row number, Timer: 4-bit timer,
PR: partially restored, V: valid
If the last access-to-access interval is small (e.g., <16ms),
the next one would highly likely to be small (i.e., 98%)
Chart: Normalized Performance
| Memory Non-Intensive | Memory Intensive | 25% Memory Intensive | 50% Memory Intensive | 75% Memory Intensive | 100% Memory Intensive
CC | 1.0023 | 1.0684 | 1.0169 | 1.0689 | 1.1156 | 1.1286
RT | 1.0037 | 1.0622 | 1.0156 | 1.0645 | 1.1081 | 1.1223
CCRT | 1.0041 | 1.0846 | 1.0203 | 1.0775 | 1.129 | 1.1423
GreedyPR | 1.0051 | 1.094 | 1.0271 | 1.0971 | 1.1485 | 1.1769
CAL | 1.01 | 1.1388 | 1.0376 | 1.1304 | 1.2034 | 1.2281
IdealCAL | 1.0175 | 1.1644 | 1.0509 | 1.1753 | 1.2622 | 1.2824
Single-core
8-core
Chart: Energy Breakdown
| Base | CC | RT | CAL | Base | CC | RT | CAL | Base | CC | RT | CAL | Base | CC | RT | CAL | Base | CC | RT | CAL | Base | CC | RT | CAL
CPU | 0.31 | 0.30938 | 0.30907 | 0.30693 | 0.2 | 0.18692 | 0.18779 | 0.17544 | 0.285 | 0.27941 | 0.27996 | 0.27404 | 0.272 | 0.25965 | 0.26384 | 0.24071 | 0.217 | 0.20029 | 0.20159 | 0.18083 | 0.19 | 0.17233 | 0.17423 | 0.15323
Cache | 0.06 | 0.05988 | 0.05982 | 0.059406 | 0.085 | 0.079439 | 0.079812 | 0.074561 | 0.065 | 0.063726 | 0.06385 | 0.0625 | 0.069 | 0.065867 | 0.06693 | 0.061062 | 0.081 | 0.074763 | 0.075249 | 0.0675 | 0.087 | 0.078909 | 0.079779 | 0.070161
Off-chip Link | 0.33 | 0.32934 | 0.32901 | 0.32673 | 0.39 | 0.36449 | 0.3662 | 0.34211 | 0.345 | 0.33824 | 0.33889 | 0.33173 | 0.346 | 0.33029 | 0.33562 | 0.30619 | 0.375 | 0.34613 | 0.34837 | 0.3125 | 0.384 | 0.34829 | 0.35213 | 0.30968
ACT/PRE | 0.084 | 0.083832 | 0.083748 | 0.082877 | 0.096 | 0.08972 | 0.090141 | 0.080913 | 0.0864 | 0.084707 | 0.084871 | 0.081966 | 0.0888 | 0.084768 | 0.086136 | 0.075189 | 0.0972 | 0.089716 | 0.090299 | 0.076599 | 0.1032 | 0.093602 | 0.094634 | 0.078398
RD/WR | 0.054 | 0.053892 | 0.053838 | 0.053278 | 0.063 | 0.058878 | 0.059155 | 0.053099 | 0.0558 | 0.054706 | 0.054812 | 0.053568 | 0.0588 | 0.05613 | 0.057036 | 0.051038 | 0.0618 | 0.057041 | 0.057412 | 0.04944 | 0.0648 | 0.058774 | 0.059422 | 0.050544
Ref | 0.042 | 0.042 | 0.042 | 0.042 | 0.036 | 0.036 | 0.036 | 0.036 | 0.0408 | 0.0408 | 0.0408 | 0.0408 | 0.0402 | 0.0402 | 0.0402 | 0.0402 | 0.0372 | 0.0372 | 0.0372 | 0.0372 | 0.0354 | 0.0354 | 0.0354 | 0.0354
Idle | 0.12 | 0.11982 | 0.11972 | 0.11877 | 0.13 | 0.12307 | 0.12353 | 0.11334 | 0.122 | 0.12014 | 0.12032 | 0.11756 | 0.1252 | 0.12073 | 0.12225 | 0.11095 | 0.1308 | 0.12264 | 0.12327 | 0.10883 | 0.1356 | 0.12518 | 0.1263 | 0.10956
Mem
Non-Intensive
Mem Intensive
25%
Mem Intensive
50%
Mem Intensive
75%
Mem Intensive
100%
Mem Intensive