## Slide 1: Video
Lecture 9
http://www.cs.rutgers.edu/~sn624/352-F24
Srinivas Narayana

## Slide 2: Digital representation of audio and video

## Slide 3: Digital representation of audio
Must convert analog signal to digital representation
Sample
  How many times (twice the max frequency in the signal)
Quantize
  How many levels or bits to represent each sample
  More levels  more accurate representation of signal
  More levels  more bits to store & need more bandwidth to transmit
Compress
  Compact representation of quantized values
3

## Slide 4: Audio representation
analog audio signal sampled at constant rate
  telephone: 8,000 samples/sec
  CD music: 44,100 samples/sec
each sample quantized, i.e., rounded
  e.g., 28=256 possible quantized values
  each quantized value represented by bits, e.g., 8 bits for 256 values
time
audio signal amplitude
analog
signal
quantized value of
analog value
quantization error
sampling rate
(N sample/sec)

## Slide 5: Audio representation
example: 8,000 samples/sec, 256 quantized values
Bandwidth needed: 64,000 bps
receiver converts bits back to analog signal:
  some quality reduction
Example rates
CD: 1.411 Mbps
MP3: 96, 128, 160 Kbps
Internet telephony: 5.3 Kbps and up
time
audio signal amplitude
analog
signal
quantized value of
analog value
quantization error
sampling rate
(N sample/sec)

## Slide 6: Video representation
Video: sequence of images displayed at constant rate
  e.g., 30 images/sec
  Appear continuous due to the stroboscopic effect
frame i
frame i+1

## Slide 7: Video representation
Digital image: array of pixels
  each pixel represented by bits
  Encode luminance and color
  Number of pixels: resolution
Coding: use redundancy within and between images to decrease # bits used to encode image
  spatial (within image)
  temporal (from one image to next)
Encoding/decoding algorithm
often called a codec
……………………...…
spatial coding example: instead of sending N values of same color (all purple), send only two values: color value (purple) and number of repeated values (N)
……………………...…
frame i
frame i+1
temporal coding example: instead of sending complete frame at i+1, send only differences from frame i (motion vectors)

## Slide 8: Video codecs: terminology
Video bit rate: effective number of bits per second of the video after encoding
It depends on many factors
  Resolution of each image: more pixels = more bits
  Detail per pixel: more luminance & color detail = more bits
  Amount of movement in the video. More movement = more bits
  Quality of overall compression in the codec
Video bit rate is typically correlated with quality of perception
  Higher bit rate == better to perceive

## Slide 9: Bit-rates: terminology
Bit-rate of a video changes over the duration of the video
CBR: (constant bit rate): fixed bit-rate video
VBR: (variable bit rate): different parts of the video have different bit rates, e.g., changes in color, motion, etc.
  For VBR, we talk about average bit-rate over video’s duration
Examples of average video bit-rates
  MPEG 1 (CD-ROM) 1.5 Mbps. MPEG2 (DVD) 3-6 Mbps
  MPEG4 (often used in Internet, < 1 Mbps)
  In general, one Internet video stream takes up a few Mbit/s (more for HD)
https://blog.video.ibm.com/streaming-video-tips/what-is-video-encoding-codecs-compression-techniques/

## Slide 10: Networking multimedia: 3 types
On-demand streamed video/audio
  Can begin playout before downloading the entire file
  Ful video/audio stored at the server: able to transmit faster than audio/video will be rendered (with storing/buffering at client)
  e.g., Spotify, YouTube, Netflix
Conversational voice or video over IP
  interactive human-to-human communication limits delay tolerance
  e.g., Zoom
Live streamed audio, video
  e.g, sporting event on sky sports
  Can delay a little, but must be close to the “live edge” of content

## Slide 11: On-demand Video Streaming

## Slide 12: Streaming (stored) video
Media is prerecorded at different qualities
  Available in storage at the server
Client downloads an initial portion and starts viewing
  The rest is downloaded as time progresses
  No need for user to wait for entire content to be downloaded (streaming)
Can change the quality of the content and where it’s fetched mid-stream

## Slide 13: Streaming stored video
video
recorded (e.g., 30 frames/sec)
2. video
sent
Cumulative data (e.g. bytes)
streaming: at this time, client
playing out early part of video,
while server still sending later
part of video
network delay
(fixed in this example)
time
3. video received,
played out at client
(30 frames/sec)
Server
e.g. Netflix
Client
e.g., your phone
Constant bit rate video

## Slide 14: Streaming stored video: challenges
Continuous playout constraint: once video playout begins at client, time gap between frames must match the original time gap in the video (why?)
But network delays are variable!
Clients have a client-side buffer of downloaded video to absorb variation in network delay, available bandwidth
The video buffer also helps with user interactions: pause, fast-forward, rewind, jump through video

## Slide 15: Introduce a delay for smooth playout
constant bit
rate video
transmission
Cumulative data
time
variable
network
delay
client video
reception
constant bit
rate video
playout at client
client playout
delay
buffered
video
Client-side buffering with playout delay:
compensate for variations in the network delay

## Slide 16: But not too small a delay
constant bit
rate video
transmission
Cumulative data
time
variable
network
delay
client video
reception
constant bit
rate video
playout at client
client playout
delay
buffered
video
Playout delay that’s too small can cause stalls
There’s nothing in the buffer to show to the user