## Slide 1: Flow Control; Congestion Control
Lecture 16
http://www.cs.rutgers.edu/~sn624/352-F24
Srinivas Narayana

## Slide 2: How much data to keep in flight?
Stop and Wait
RTT
RTO
SEQ 0
SEQ 1
Retransmit
ACK
SEQ 0
RTT
SEQ 1
SEQ 2
SEQ 3
ACK 1
ACK 2
ACK 3
ACK 4
Pipelined Reliability
= window size
Proportional to throughput

## Slide 3
application
process
TCP socket
receiver buffers
TCP
code
receiver
from sender
recv()
sender
Multiple locations for bottlenecks
What’s the bottleneck? How to adapt how much data to keep in flight?
Flow Control
Congestion Control
Flow Control: Receiver informs sender free buffer over time
0
1
2
3
4
5
6
7
1
0
Last cumulative
ACK’ed seq #
Last transmitted
seq #
Window <= Advertised window
Sender’s view:
How to size this buffer?

## Slide 4: TCP flow control
If receiver app is too slow reading data:
  receiver socket buffer fills up
  => advertised window shrinks
  => sender’s window (sending rate) reduces
  => sender’s socket buffer fills up
  => sender process put to sleep upon send()
Sender
Receiver
1
2
3
4
1
2
4
5
3
0
1
2
3
4
5
6
7
1
0
Last cumulative
ACK’ed seq #
Last transmitted
seq #
Window <= Advertised window
Sender’s view:

## Slide 5: TCP flow control
Flow control matches the sending process’s write speed to the receiving process’s read speed.
Sender
Receiver
1
2
3
4
1
2
4
5
3
0
1
2
3
4
5
6
7
1
0
Last cumulative
ACK’ed seq #
Last transmitted
seq #
Window <= Advertised window
Sender’s view:

## Slide 6: Sizing the receiver’s socket buffer
Operating systems have a default receiver socket buffer size
  Listed among sysctl –a | grep net.inet.tcp on MAC
  Listed among sysctl –a | grep net.ipv4.tcp on Linux
If socket buffer is too small, sender can’t keep too many packets in flight  lower throughput
If socket buffer is too large, too much memory consumed per socket
How big should the receiver socket buffer be?

## Slide 7: Sizing the receiver’s socket buffer
Case 1: Suppose the receiving app is reading data too slowly:
No amount of receiver buffer can prevent low throughput (for a long-lived connection).
Flow control matches throughput to the receiving app’s (low) speed

## Slide 8: Sizing the receiver’s socket buffer
Case 2: Suppose the receiving app reads sufficiently fast on average to match the sender’s writing speed.
  Assume the sender desires a window of size W.
  The receiver must use a buffer of size at least W. Why?
Captures two cases:
(1) When the first sequence #s in the window are dropped
  Selective repeat: data in window buffered until the “hole” within the window can be filled by the sender. Advertised window reduces sender’s window
(2) When the sender sends a burst of data of size W
  The receiver may not keep up with the instantaneous rate of the sender
Set receiver socket buffer size > desired window size

## Slide 9: Summary of flow control
Keep memory buffers available at the receiver whenever the sender transmits data
Buffers needed to hold for selective repeat, reassembling data in order, and until applications can read data
Inform available buffer to sender on an ongoing basis, with each ACK
Function: match sender speed to receiver speed
Correct socket buffer sizing is important for TCP throughput
  Throughput = window size / RTT <= receiver socket buffer / RTT

## Slide 10: Info on (tuning) TCP stack parameters
https://www.ibm.com/support/knowledgecenter/linuxonibm/liaag/wkvm/wkvm_c_tune_tcpip.htm
https://cloud.google.com/solutions/tcp-optimization-for-network-performance-in-gcp-and-hybrid

## Slide 11: Playing around with socket buffer sizes
iperf –s ; iperf –c localhost –i 1
ping localhost
sudo tc qdisc add dev lo root netem delay 100ms
sudo sysctl net.ipv4.tcp_rmem # min, default, max
Default buffer size 128KB; change e.g., 2.56MB by using
  sudo sysctl net.ipv4.tcp_rmem=“4096 2621440 6291456”
Clean up and restore to defaults
sudo tc qdisc del dev lo root netem
  If needed:
  sudo sysctl net.ipv4.tcp_rmem=“4096 131072 6291456”

## Slide 12: Congestion Control

## Slide 13: Congestion
Amount of useful data that gets across to the receiver
Fraction of link used (link load)
~100%
Queueing delay
Link load
~100%
Packets get dropped beyond max buffer
Max amount of useful data that link can support, ie. link bandwidth
Too many retransmissions due to packet drops!
The amount of useful (fresh) data plummets.
Congestion collapse
(occurred for real on the Internet in the last 80s)
∞
Routers have buffers which accommodate queued packets.
https://en.wikipedia.org/wiki/Network_congestion#Congestive_collapse

## Slide 14: How should multiple endpoints share net?
It is difficult to know where the bottleneck link is
It is difficult to know how many other endpoints are using that link
Endpoints may join and leave at any time
Network paths may change over time, leading to different bottleneck links (with different link rates) over time