## Slide 1: Routers; LPM; Protocols
Lecture 22
http://www.cs.rutgers.edu/~sn624/352-F24
Srinivas Narayana

## Slide 2: Review: Router architecture
high-speed
switching
fabric
route
processor
router input ports
router output ports
Control plane
Data plane
Forwarding function: move packets from one input port to another.
assuming distributed routing, routing function: decide which ports packets need to exit

## Slide 3: Fabrics: Types
…
…
Switching fabric
Input port
Input port
Input port
Output port
Output port
Output port
Input port writes packets into shared memory.
Output port reads the packet when output link ready to transmit.
Single shared channel to move data from input to output port.
Easy to build buses; technology is quite mature.
Each input port has a physical data path to every output port.
Switch at the cross-over points turns on to connect pairs of ports.
Fabric goal: Ferry as many packets as possible from input to output ports as quickly as possible.

## Slide 4: Fabrics: Types
…
…
Switching fabric
Input port
Input port
Input port
Output port
Output port
Output port
Modern high-speed routers use highly optimized shared-memory-based interconnects.
Crossbars can get expensive as the number of ports grows (N2 connections for N ports)
MGR uses a crossbar and schedules (in,out) port pairs.

## Slide 5: Nonblocking fabrics
High-speed switching fabrics designed to be nonblocking:
  If an output port is “available”, an input port can always transmit to it without being blocked by the switching fabric itself
  Nontrivial to achieve
Crossbars are nonblocking by design
Shared memory can be designed to be nonblocking if memory accesses can be made fast enough
…
…
Switching fabric
Input port
Input port
Input port
Output port
Output port
Output port

## Slide 6: Nonblocking fabrics
With a nonblocking fabric, queues aren’t formed due to the switching fabric.
  With a nonblocking fabric, there are no queues due to inefficiencies at the input port or the switching fabric
Queues only form due to contention for the output port
  Fundamental, unavoidable, given the route
…
…
Switching fabric
Input port
Input port
Input port
Output port
Output port
Output port

## Slide 7: Nonblocking fabrics
With a nonblocking fabric, queues aren’t formed due to the switching fabric.
  With a nonblocking fabric, there are no queues due to inefficiencies at the input port or the switching fabric
Queues only form due to contention for the output port
  Fundamental, unavoidable, given the route
Typically, these queues form on the output side
  But can also “backpressure” to the input side if there is high contention for the output port
  i.e.: can’t move pkts to output Qs since buffers full, so buffer @ input
…
…
Switching fabric
Input port
Input port
Input port
Output port
Output port
Output port

## Slide 8: Control (plane) processor
A general-purpose processor that “programs” the data plane:
  Forwarding table
  Scheduling and buffer management policy
Implements the routing algorithm by processing routing protocol messages
  Mechanism by which routers collectively solve the Internet routing problem
  More on this soon.
…
…
Switching fabric
Input port
Input port
Input port
Output port
Output port
Output port
Control Processor

## Slide 9
Routing
Algorithm
data
plane
control
plane
1
2
0111
values in arriving
packet header, i.e, destination IP address
3
Data plane
per-packet processing
(~ tens of nanoseconds)
Control plane
Traditional distributed routing: per route-change processing
(~ a few tens of seconds)
Router design: the bigger picture

## Slide 10: Longest Prefix Matching

## Slide 11: Review: Route lookup
Table lookup matches a packet against an IP prefix
  Ex: 65.12.45.2 matches 65.0.0.0/8
Prefixes are allocated to organizations by Internet registries
But organizations can reallocate a subset of their IP address allocation to other orgs
Outgoing Port
Dst-network
Port
Forwarding Table
Route Lookup Data Structure
65.0.0.0/8
128.9.0.0/16
149.12.0.0/19
3
1
7
Parse
Transport
Network
Link layer
Extract destination IP address

## Slide 12: Example of IP block reallocation
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
ISP A
Organization 1
Organization 8
Internet
Organization 2
200.23.20.0/23
Organization 3
.
.
.
.
.
.
ISP A owns the IP block 200.23.16.0/20.
Suppose ISP A reallocates a part of its IP block to orgs 1… 8
Dst IP Prefix | Output port
65.0.0.0/8 | 3
128.9.0.0/16 | 1
… | …
200.23.16.0/20 | 7 (towards A)
There is an announcement mechanism (BGP) by which ISP A can inform the rest of the Internet about the prefixes it owns.
It is enough to announce a coarse-grained prefix 200.23.16.0/20 rather than 8 separate sub-prefixes.
[BGP] Send me pkts destined to
200.23.16.0/20
Route Aggregation
Save forwarding table memory
Fewer routing protocol msgs
ISP = Internet Service Provider

## Slide 13: Example of IP block reallocation
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
ISP A
Organization 1
Organization 8
Internet
Organization 2
200.23.20.0/23
Organization 3
.
.
.
.
.
.
ISP A owns the IP block 200.23.16.0/20.
Suppose ISP A reallocates a part of its IP block to orgs 1… 8
Dst IP Prefix | Output port
65.0.0.0/8 | 3
128.9.0.0/16 | 1
… | …
200.23.16.0/20 | 7 (towards A)
Now suppose one of these organizations adds another ISP for its Internet service and prefers using the new ISP.
Note: it’s possible for the organization to retain its assigned IP block.
[BGP] Send me pkts destined to
200.23.16.0/20

## Slide 14: Example of IP block reallocation
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
ISP A
Organization 1
Organization 8
Internet
Organization 2
200.23.20.0/23
Organization 3
.
.
.
.
.
.
ISP A owns the IP block 200.23.16.0/20.
Suppose ISP A reallocates a part of its IP block to orgs 1… 8
Dst IP Prefix | Output port
65.0.0.0/8 | 3
128.9.0.0/16 | 1
… | …
200.23.16.0/20 | 7 (towards A)
200.23.18.0/23
Organization 2
ISP B
[BGP] Announce 200.23.18.0/23
(besides other IP prefixes)
[BGP] Send me pkts destined to
200.23.16.0/20

## Slide 15: Example of IP block reallocation
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
ISP A
Organization 1
Organization 8
Internet
Organization 2
200.23.20.0/23
Organization 3
.
.
.
.
.
.
ISP A owns the IP block 200.23.16.0/20.
Suppose ISP A reallocates a part of its IP block to orgs 1… 8
Dst IP Prefix | Output port
65.0.0.0/8 | 3
128.9.0.0/16 | 1
200.23.18.0/23 | 4 (towards B)
200.23.16.0/20 | 7 (towards A)
200.23.18.0/23
Organization 2
ISP B
[BGP] Announce 200.23.18.0/23
(besides other IP prefixes)
[BGP] Send me pkts destined to
200.23.16.0/20

## Slide 16: A closer look at the forwarding table
200.23.18.0/23 is inside 200.23.16.0/20
A packet with destination IP address 200.23.18.xx is in both prefixes
  i.e., both entries match
Q: How should the router choose to forward the packet?
  Ideally: The org prefers B, so should choose B
Dst IP Prefix | Output port
65.0.0.0/8 | 3
128.9.0.0/16 | 1
200.23.18.0/23 | 4 (towards B)
200.23.16.0/20 | 7 (towards A)
200.23.16.0/20
The Internet uses a policy to prioritize: Longest Prefix Matching

## Slide 17: Longest Prefix Matching (LPM)
Use the longest matching prefix, i.e., the most specific route, among all prefixes that match the packet.
Policy borne out of the Internet’s IP allocation model: prefixes and sub-prefixes are handed out
Internet routers use longest prefix matching.
  How would you implement this in software?
  Interesting algorithmic and design challenges in developing software and hardware
Dst IP Prefix | Output port
65.0.0.0/8 | 3
128.9.0.0/16 | 1
200.23.18.0/23 | 4 (towards B)
200.23.16.0/20 | 7 (towards A)
200.23.16.0/20

## Slide 18
Internet routers perform longest-prefix matching on destination IP addresses of packets.

## Slide 19: Why is LPM useful?
Help organizations move in one block to a different ISP while retaining their IP prefix assignment.
  IPs unchanged: e.g., don’t have to update DNS for services in the org
Also enable an organization (e.g. Rutgers) to connect to two or more Internet Service Providers (ISPs) and express routing preferences
  Announce longer prefixes to make the rest of the Internet prefer a certain path

## Slide 20: Why is LPM useful?
An ISP (e.g., Verizon) has allocated a sub-prefix (or “subnet”) of a larger prefix that the ISP owns to an organization (e.g., Rutgers)
Further, the ISP announces the aggregated prefix to the Internet to save on number of forwarding table memory and number of announcements
The organization (e.g., Rutgers) is reachable over multiple paths (e.g., through another ISP like AT&T)
The organization has a preference to use one path over another, and expresses this by announcing the longer (more specific) prefix
Routers in the Internet must route based on the longer prefix
Rutgers
Verizon
AT&T
Agg. route
Specific route
(longer prefix)

## Slide 21: IPv4 Datagram Format

## Slide 22
ver
length
32 bits
data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
32-bit source IP address
IP protocol version
number
header length
(bytes)
max number
remaining hops
(decremented at
each router)
for
fragmentation/
reassembly
total datagram
length (bytes)
upper layer protocol to deliver payload to, e.g., TCP, UDP
hdr
len
type of
service
Bits for
traffic differentiation
e.g., audio, web, bulk
flags
fragment
offset
upper
protocol
32-bit destination IP address
Options (if any)
E.g. timestamp,
record the route
taken, specify
list of routers
to visit (“source routing”)
How much header overhead?
(default) 20 bytes of TCP
(default) 20 bytes of IP
= 40 bytes
Transport
Network
Link layer

## Slide 23
The network layer is all about reachability.
We’ll see protocols that solve subproblems.
How does an endpoint get an address?
DHCP
How does an endpoint talk to another within the same network?
ARP
How does an endpoint talk to another outside its network?
Routing protocols
OSPF, RIP, BGP
Gateways
NAT & IPv6
Debugging?
ICMP

## Slide 24: IP Support Protocols
Many support protocols and mechanisms for the network layer
  Protocols: DHCP, ICMP, ARP, IPv6, …
  Mechanisms: NAT
Some of these protocols use an IP header underneath their own header (ICMP) or replace the IP header with their own (ARP)
  But these shouldn’t be construed as transport/network protocols
  They are fundamental to supporting IP/network layer functionality
  More appropriately discussed as support protocols for the network layer

## Slide 25: Internet Control Message Protocol (ICMP)

## Slide 26: Internet Control Message Protocol
A protocol for troubleshooting and diagnostics
Works over IP: unreliable delivery of packets
Some functions of ICMP:
  Determine reachability and network errors
  Specify that packets have been in the network for too long

## Slide 27: ICMP message format (informal)
IP header
ICMP header
Message type, Code, Checksum,
ICMP data
https://en.wikipedia.org/wiki/Internet_Control_Message_Protocol#Control_messages

## Slide 28: Specific uses of ICMP
Echo request reply
  Check remotely if an endpoint is alive and connected
  Without running an app remotely or controlling that endpoint
An unreachable destination
  Invalid address and/or port
Knowing if packet’s IP time-to-live expired
  Example, due to routing loops
Look at two tools built using ICMP: ping and traceroute