## Slide 1: Routing (part 2)
Lecture 24
http://www.cs.rutgers.edu/~sn624/352-F24
Srinivas Narayana

## Slide 2
Routing: Google Maps for the Internet?
Goals of routing:
#1 Good paths
#2 Failure resilience
Distance vector protocols
Routing protocols
Link state
protocols
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
Flooding
v
w
u
D(w),
known least
c(w, v)
D(v),
estimate
Dijkstra’s algorithm
Relaxation
Q1. What info exchanged?
Q2. What computation?

## Slide 3: Distance Vector Protocols

## Slide 4: Distance Vector Protocol
Each router only exchanges a distance vector with its neighbors
  Distance: how far the destination is
  Vector: a value for each destination
DVs are only exchanged between neighbors; not flooded
Use incomplete view of graph derived from neighbors’ distance vectors to compute the shortest paths
Distance vector protocols
Routing protocols
Link state
protocols
Q1. What info exchanged?
Q2. What computation?

## Slide 5: Q1: Distance Vectors
Dx(y) = estimate of least cost from x to y
Distance vector: Dx = [Dx(y): y є N ]
Node x knows cost of edge to each neighbor v: c(x,v)
Node x maintains Dx
Node x also maintains its neighbors’ distance vectors
  For each neighbor v, x maintains Dv = [Dv(y): y є N ]
Nodes exchange distance vector periodically and whenever the local distance vector changes (e.g., link failure, cost changes)
Notes: At each node we need
- an array (known as DV) that lists the current least costs to reach all known destinations
- also need to maintain the next-hop along the least cost path
- the DV’s from all neighbors

## Slide 6: Q2: Algorithm
Bellman-Ford algorithm
Each node initializes its own distance vector (DV) to edge costs
Each node sends its DVs to its neighbors
When a node x receives new DV from a neighbor v, it updates its own DV using the Bellman-Ford equation:
Given dx(y) := estimated cost of the least-cost path from x to y
Update dx(y) = minv {c(x,v) + dv(y) }
cost to reach neighbor v directly from x
minimum taken over
all neighbors v of x
cost of path from neighbor v to destination y

## Slide 7: Visualization
Which neighbor v offers the current best path from x to y?
Path through neighbor v has cost c(x,v) + dv(y)
Choose min-cost neighbor
Remember min-cost neighbor as the one used to reach node y
This neighbor determines the output port!
x
v
y
c(x,v)
Neighbor v sends its distance vector to x.
dv(y)
v’
v’’
v’’’
Use v’’ and link (x,v’’) to reach y.

## Slide 8
x y z
x
y
z
0 2 7
∞
∞
∞
∞
∞
∞
from
cost to
from
from
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
∞
∞
∞
∞
∞
cost to
x y z
x
y
z
0 2 7
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 7
from
cost to
x y z
x
y
z
∞
∞
∞
7
1
0
cost to
2 0 1
∞ ∞ ∞
2 0 1
7 1 0
2 0 1
7 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
time
x
z
1
2
7
y
node x table
node y table
node z table
Dx(y) = min{c(x,y) + Dy(y), c(x,z) + Dz(y)} = min{2+0 , 7+1} = 2
Dx(z) = min{c(x,y) + Dy(z),
c(x,z) + Dz(z)}
= min{2+1 , 7+0} = 3
∞
Notes: This example assumes that nodes are computing routes in a lock-step fashion.

## Slide 9: Good news travels fast
Suppose the link cost reduces or a new better path becomes available in a network.
The immediate neighbors of the change detect the better path immediately
Since their DV changed, these nodes notify their neighbors immediately.
  And those neighbors notify still more neighbors
  … until the entire network knows to use the better path
Good news travels fast through the network
This is despite messages only being exchanged among neighbors
x
z
1
4
2
y
1

## Slide 10: Bad news travels slowly
If router goes down, could be a while before network realizes it.
A
B
C
D
E
1
2
3
4
3
2
3
4
3
4
3
4
5
4
5
4
5
6
5
6
7
6
7
6
Initially
After 1 exchange
After 2 exchanges
After 3 exchanges
After 4 exchanges
After 5 exchanges
etc… to infinity
Count to infinity problem
B still thinks it can reach A through C… bad!
C thinks it can reach A through B… worse!
B, D think they can reach A through C… ugly!

## Slide 11: Bad news travels slowly
Reacting appropriately to bad news requires information that only other routers have. DV does not exchange sufficient info.
B needs to know that C has no other path to A other than via B.
DV does not exchange paths; just distances!
Poisoned reverse: if X gets its route to Y via Z, then X will announce dX(Y) = ∞ in its message to Z
  Effect: Z won’t use X to route to Y
  However, this won’t solve the problem in general (think why.)
A
B
C
D
E

## Slide 12: Summary: Comparison of LS and DV
Link State Algorithms
Nodes have full visibility into the network’s graph
Copious message exchange: each LSA is flooded over the whole network
Robust to network changes and failures
Distance Vector Algorithms
Only distances and neighbors are visible
Sparse message exchange: DVs are exchanged among neighbors only
Brittle to router failures. Incorrect info may propagate all over net
OSPF
Open Shortest Path First
(v2 RFC 2328)
EIGRP
Enhanced Interior Gateway Routing Protocol
(RFC 7868)

## Slide 13
Distance vector protocols
Routing protocols
Link state
protocols
Every router is aware of the existence of every other router.
Messages reveal information on the full network (graph) structure.
Message exchange and forwarding tables scale with network size.
These assumptions/settings cannot work on the Internet.

## Slide 14: Internet Routing

## Slide 15: The Internet is a large federated network
AT&T
Comcast
Verizon

## Slide 16: The Internet is a large federated network
AT&T
Comcast
Verizon
Several autonomously run organizations: No one “boss”
Organizations cooperate, but also compete
e.g., AT&T has little commercial interest in revealing its internal network structure to Verizon.

## Slide 17: The Internet is a large federated network
AT&T
Comcast
Verizon
Several autonomously run organizations: No one “boss”
Organizations cooperate, but also compete
Message exchanges must
not reveal internal network details.
Algorithm must work with “incomplete” information about its neighbors’ internal topology.

## Slide 18: The Internet is a large federated network
AT&T
Comcast
Verizon
Internet today: > 70,000 unique autonomous networks
Internet routers: > 800,000 forwarding table entries
Keep messages & tables as small as possible. Don’t flood
Algorithm must be incremental: don’t recompute the whole table on every message exchanged.