## Slide 1: Routing (part 3)
Lecture 25
http://www.cs.rutgers.edu/~sn624/352-F24
Srinivas Narayana

## Slide 2
The network layer enables reachability.
We’ll see protocols that solve subproblems.
How does an endpoint get an address?
DHCP
How does an endpoint talk to another within the same network?
ARP
How does an endpoint talk to another outside its network?
Routing protocols
OSPF, RIP, BGP
Gateways
NAT
Debugging?
ICMP

## Slide 3
Distance vector protocols
Routing protocols
Link state
protocols
Every router is aware of the existence of every other router.
Messages reveal information on the full network (graph) structure.
Message exchange and forwarding tables scale with network size.
These assumptions/settings cannot work on the Internet.

## Slide 4: The Internet is a large federated network
AT&T
Comcast
Verizon
Several autonomously run organizations: No one “boss”
Organizations cooperate, but also compete
e.g., AT&T has little commercial interest in revealing its internal network structure to Verizon.

## Slide 5: The Internet is a large federated network
AT&T
Comcast
Verizon
Several autonomously run organizations: No one “boss”
Organizations cooperate, but also compete
Message exchanges must
not reveal internal network details.
Algorithm must work with “incomplete” information about its neighbors’ internal topology.

## Slide 6: The Internet is a large federated network
AT&T
Comcast
Verizon
Internet today: > 70,000 unique autonomous networks
Internet routers: > 800,000 forwarding table entries
Keep messages & tables as small as possible. Don’t flood
Algorithm must be incremental: don’t recompute the whole table on every message exchanged.

## Slide 7: Inter-domain Routing
Routing approaches so far (LS + DV) are applicable within one autonomous system (AS), e.g., Rutgers
  Called intra-domain routing protocols
The Internet uses Border Gateway Protocol (BGP)
All AS’es speak BGP. It is the glue that holds the Internet together
BGP is a path vector protocol
Distance vector protocols
Routing protocols
Link state
protocols
Path vector protocols
Messages?
Algorithm?

## Slide 8: Q1. BGP Messages
Routing Announcements or Advertisements
  “I am here” or “I can reach here”
  Occur over a TCP connection (BGP session) between routers
Route announcement = destination + attributes
  Destination: IP prefix
Route Attributes:
  AS-level path
  Next hop
  Several others: origin, MED, community, etc.
An AS promises to use advertised path to reach destination
Only route changes are advertised after BGP session established
2b
2d
2c
2a
X
“I am here.”
Dst: 128.1.2.0/24
AS path: X
“I can reach X”
Dst: 128.1.2.0/24
AS path: AS2, X
AS 2
1b
1d
1c
1a
No link metrics, distances!
Exchange paths: path vector
Loop detection is easy
(no “count to infinity”)

## Slide 9: Q1. Next Hop
Next hop conceptually denotes the first router interface that begins the AS-level path
  The meaning of this attribute is context-dependent
In an announcement arriving from a different AS (eBGP), next hop is the router in the next AS which sent the announcement
  Example: Next Hop of the eBGP announcement reaching 1c is 2a
1b
1d
1c
1a
2b
2d
2c
2a
AS 1
AS 2
eBGP announcement:
AS2, X
X

## Slide 10: Q1. Next Hop
Suppose router 1c imports the path (more on this soon)
Router 1c will propagate the announcement inside the AS using iBGP
The next hop of this (iBGP) announcement is set to 1c
  In particular, the next hop is an AS1 internal address
1b
1d
1c
1a
2b
2d
2c
2a
AS 1
AS 2
eBGP announcement:
AS2, X
X

## Slide 11: Q2. The algorithm
A BGP router does not consider every routing advertisement it receives by default to make routing decisions!
  An import policy determines whether a route is even considered a candidate
Once imported, the router performs route selection
A BGP router does not propagate its chosen path to a destination to all other AS’es by default!
  An export policy determines whether a (chosen) path can be advertised to other AS’es and routers
Policy considerations make BGP very different from intra-domain (LS / DV) protocols
Programmed by network operator

## Slide 12: Policies in BGP

## Slide 13: Policy arises from business relationships
Customer-provider relationships:
  E.g., Rutgers is a customer of AT&T
Peer-peer relationships:
  E.g., Verizon is a peer of AT&T
Business relationships depend on where connectivity occurs
  “Where”, also called a “point of presence” (PoP)
  e.g., customers at one PoP but peers at another
  Internet-eXchange Points (IXPs) are large PoPs where ISPs come together to connect with each other (often for free)

## Slide 14: BGP Export Policy
A,B,C are provider networks
X,W,Y are customers (of provider networks)
X is dual-homed: attached to two networks
policy to enforce: X does not want to route from B to C via X
  So, X will not announce to B a route to C
A
B
C
W
X
Y
legend:
customer
network:
provider
network
Suppose an ISP only wants to route traffic to/from its customer networks (does not want to carry transit traffic between other ISPs)

## Slide 15: BGP Export Policy
A announces path Aw to B and to C
B will not announce BAw to C:
  B gets no “revenue” for routing CBAw, since none of C, A, w are B’s customers
C will route CAw (not using B) to get to w
A
B
C
W
X
Y
legend:
customer
network:
provider
network
Suppose an ISP only wants to route traffic to/from its customer networks (does not want to carry transit traffic between other ISPs)

## Slide 16: Thumb rules for export policy
Export customer-learned routes to the rest of the Internet
  Financially attractive if the Internet uses your AS to get to a customer
  OK to export customer-learned route to a provider since the customer must be reachable from the rest of the Internet
Do not export a provider-learned route to another provider
  Don’t lose money on both sides
Do not export peer-learned route to another peer
  The resources of your AS are used but no financial gains from free “transit” service
OK to export provider-learned route to a customer
  Customer must be able to reach the rest of the Internet
  Also financially attractive