## Slide 1: Streaming multimedia
CS 352, Lecture 22
http://www.cs.rutgers.edu/~sn624/352-S19
Srinivas Narayana
(heavily adapted from slides by Prof. Badri Nath and the textbook authors)

## Slide 2: Multimedia networking
Many applications on the Internet use audio or video
IP video traffic will be 82 percent of all IP traffic […] by 2022, up from 75 percent in 2017
Internet video surveillance traffic will increase sevenfold between 2017 to 2022
Internet video to TV will increase threefold between 2017 to 2022.
Consumer Video-on-Demand (VoD) traffic will nearly double by 2022
2
Source: Cisco visual networking index 2017--22

## Slide 3: What’s different about these applications?
Traditional applications (HTTP(S), SMTP)
  Delay tolerant but not loss tolerant
  Data used after transfer complete
But multimedia applications are often “real time”
  Data delivery time during transfer has implications
Video/audio streaming
  Delay-sensitive
Real-time audio and video
  Delays > 400 ms for audio is a bad user experience
  Somewhat loss tolerant
3

## Slide 4: Digital representation of audio and video

## Slide 5: Digital representation of audio
Must convert analog signal to digital representation
Sample
  How many times (twice the max frequency in the signal)
Quantize
  How many levels or bits to represent each sample
  More levels  more accuracy
  More levels  more bits to store & more bandwidth to transmit
Compress
  Compact representation of quantized values
5

## Slide 6: Audio representation
analog audio signal sampled at constant rate
  telephone: 8,000 samples/sec
  CD music: 44,100 samples/sec
each sample quantized, i.e., rounded
  e.g., 28=256 possible quantized values
  each quantized value represented by bits, e.g., 8 bits for 256 values
time
audio signal amplitude
analog
signal
quantized value of
analog value
quantization error
sampling rate
(N sample/sec)

## Slide 7: Audio representation
example: 8,000 samples/sec, 256 quantized values
Bandwidth needed: 64,000 bps
receiver converts bits back to analog signal:
  some quality reduction
Example rates
CD: 1.411 Mbps
MP3: 96, 128, 160 Kbps
Internet telephony: 5.3 Kbps and up
time
audio signal amplitude
analog
signal
quantized value of
analog value
quantization error
sampling rate
(N sample/sec)

## Slide 8: Video representation
Video: sequence of images displayed at constant rate
  e.g., 24 images/sec
Digital image: array of pixels
  each pixel represented by bits
Coding: use redundancy within and between images to decrease # bits used to encode image
  spatial (within image)
  temporal (from one image to next)
Coding/decoding algorithm often called a codec
……………………...…
spatial coding example: instead of sending N values of same color (all purple), send only two values: color value (purple) and number of repeated values (N)
……………………...…
frame i
frame i+1
temporal coding example: instead of sending complete frame at i+1, send only differences from frame i

## Slide 9: Video representation
……………………...…
spatial coding example: instead of sending N values of same color (all purple), send only two values: color value (purple) and number of repeated values (N)
……………………...…
frame i
frame i+1
temporal coding example: instead of sending complete frame at i+1, send only differences from frame i
Video bit rate: effective bits per second of the video after encoding
CBR: (constant bit rate): video encoding rate fixed
VBR: (variable bit rate): video encoding rate changes as amount of spatial, temporal coding changes
examples:
  MPEG 1 (CD-ROM) 1.5 Mbps
  MPEG2 (DVD) 3-6 Mbps
  MPEG4 (often used in Internet, < 1 Mbps)

## Slide 10: Multimedia networking: 3 application types
streaming, stored audio, video
  streaming: can begin playout before downloading entire file
  stored (at server): can transmit faster than audio/video will be rendered (implies storing/buffering at client)
  e.g., YouTube, Netflix, Hulu
conversational voice/video over IP
  interactive nature of human-to-human conversation limits delay tolerance
  e.g., Skype
streaming live audio, video
  e.g., live sporting event (futbol)

## Slide 11: Streaming video

## Slide 12: Streaming stored content
Media is prerecorded
Client downloads an initial portion and starts viewing
Rest downloaded as time progresses
No need to wait for entire content to be downloaded
Can change content sites mid-stream based on network conditions

## Slide 13: Streaming stored video:
video
recorded (e.g., 30 frames/sec)
2. video
sent
Cumulative data
streaming: at this time, client
playing out early part of video,
while server still sending later
part of video
network delay
(fixed in this example)
time
3. video received,
played out at client
(30 frames/sec)

## Slide 14: Streaming stored video: challenges
continuous playout constraint: once client playout begins, playback must match original timing
  … but network delays are variable (jitter), so will need client-side buffer to match playout requirements
other challenges:
  client interactivity: pause, fast-forward, rewind, jump through video
  video packets may be lost, retransmitted

## Slide 15: Streaming stored video: revisited
constant bit
rate video
transmission
Cumulative data
time
variable
network
delay
client video
reception
constant bit
rate video
playout at client
client playout
delay
buffered
video
client-side buffering and playout delay: compensate for network-added delay, delay jitter

## Slide 16: Client-side buffering, playout
variable fill
rate, x(t)
client application
buffer, size B
playout rate,
e.g., CBR r
buffer fill level, Q(t)
video server
client

## Slide 17: Client-side buffering, playout
variable fill
rate, x(t)
client application
buffer, size B
playout rate,
e.g., CBR r
buffer fill level, Q(t)
video server
client
1. Initial fill of buffer until playout begins at tp
2. playout begins at tp,
3. buffer fill level varies over time as fill rate x(t) varies and playout rate r is constant

## Slide 18: Client-side buffering, playout
playout buffering: average fill rate (x), playout rate (r):
x < r: buffer eventually empties (causing freezing of video playout until buffer again fills)
x > r: buffer will not empty, provided initial playout delay is large enough to absorb variability in x(t)
  initial playout delay tradeoff: buffer starvation less likely with larger delay, but larger delay until user begins watching
variable fill
rate, x(t)
client application
buffer, size B
playout rate,
e.g., CBR r
buffer fill level, Q(t)
video server

## Slide 19: Streaming multimedia: UDP
server sends at rate appropriate for client
  often: send rate = encoding rate = constant rate
  transmission rate can be oblivious to congestion levels
short playout delay (2-5 seconds) to remove network jitter
error recovery: application-level, time permitting
RTP [RFC 2326]: multimedia payload types
UDP traffic may not get through firewalls

## Slide 20: Streaming multimedia: HTTP/TCP
multimedia file retrieved via HTTP GET
send at maximum possible rate under TCP
fill rate fluctuates due to TCP congestion control, retransmissions (in-order delivery)
larger playout delay: smooth TCP delivery rate
HTTP/TCP passes more easily through firewalls
variable rate, x(t)
TCP send buffer
video
file
TCP receive buffer
application playout buffer
server
client

## Slide 21: Streaming multimedia with DASH
Dynamic Adaptive Streaming over HTTP
Used by Netflix and other video streaming services
Client-centric approach to video delivery
  Adaptive: Client performs video bit rate adaptation
  Dynamic: Can retrieve a single video from multiple sources
Retain benefits of existing Internet and end host systems
Server is standard HTTP server
  Provides video/audio content in multiple formats and encodings
  DASH allows the use of CDNs for data delivery

## Slide 22: Dynamic Adaptive Streaming over HTTP (DASH)

## Slide 23: DASH: Key ideas
Content chunks
Each chunk can be independently retrieved
Client-side algorithms to determine and request a varying bit rate for each chunk
  Goal: ensure good quality of service
Source: Stockhammer MMSys 2011

## Slide 24: DASH Data model
Media has several periods
Each period has several Adaptation Sets: Audio, video, close caption
Several Representations (ex: codecs, bit rates) per Adaptation set
Several Chunks/Segments per Representation

## Slide 25: Dynamic bit rate changing of streams

## Slide 26: Media Presentation Descriptor (MPD)
MPD requested over http
  Also called “manifest”
Describes all segments
Timing information and byte ranges of chunks
Client uses HTTP GET RANGE from a given AS + representation to ask a given bit rate
Client could use a different URL for each AS + representation

## Slide 27: Video Delivery using CDN
User
Front end
web-servers
Video-servers
(front end)
  1. HTTP GET request for video URL
2. HTTP reply containing html to construct the web page and a link to stream, say FLV file
3. HTTP GET request
for FLV stream
4. HTTP reply
FLV stream
Internet

## Slide 28: Server Selection
File  server mapping done in at least three ways
Dynamic DNS resolution
  DNS returns different IP addresses for a given DNS name
HTTP redirect
  Use HTTP status code 3xx [with new URL]
  Web browser does a GET from the new site
IP anycast
  Use BGP to announce the same IP address from different locations
  Client reaches “nearest” location according to inter-domain routing

## Slide 29: DASH Summary
Widely used in video streaming services
Allows independent requests per segment
  Hence, independent segment quality and data sizes
  Encoded through separate HTTP objects and corresponding HTTP byte ranges
  Combined or separate audio & video streams
Works well with CDNs
  Independent representations or chunks can be queried from different locations if needed