## Slide 1: Network Support for Quality of Service (QoS)
CS 352, Lecture 24
http://www.cs.rutgers.edu/~sn624/352-S19
Srinivas Narayana
(heavily adapted from slides by Prof. Badri Nath and the textbook authors)

## Slide 2: Review: Streaming multimedia
Watching media prerecorded at servers at multiple quality levels, ex: Netflix
Client downloads an initial portion and starts viewing/listening
Need continuous playout:
  Manage network delays through a client buffer
Playout rate must be not larger than average download rate
Predominant model: Dynamic Adaptive Streaming over HTTP
  DASH video is divided into chunks
  Each chunk can be retrieved with an independent bitrate and from an independent (CDN) location

## Slide 3: Review: Conversational multimedia
Two parties making a real-time conversation, ex: Skype
Important to bound playout delays & adapt to loss
  More than ~400 ms audio delay provides for a very poor experience
Fixed and adaptive playout delays at the granularity of “talk spurts”
Retransmissions not really effective to conceal loss
  Forward error correction mechanisms
Relay-based call routing: used by Skype
  Useful to overcome NATs
  But need extra infrastructure to make it work

## Slide 4: Network support
How can the network benefit multimedia network transfers?

## Slide 5: Network support for Multimedia
A best effort Internet architecture does not offer any guarantees on delay, bandwidth, and loss
  Network may drop, reorder, corrupt packets
  Network may treat transfers randomly regardless of their “importance”
However, multimedia apps require delay and loss bounds
How to provide quality of service (QoS) for multimedia applications through network mechanisms?
  Provision enough resources: make the best of best effort service
  Mechanisms to handle traffic differently based on importance
Result: specific protocols and architectures for QoS

## Slide 6: Dimensioning best effort networks
approach: deploy enough link capacity so that congestion doesn’t occur, multimedia traffic flows without delay or loss
  low complexity of network mechanisms (use current “best effort” network)
  high bandwidth costs
challenges:
  network dimensioning: how much bandwidth is “enough?”
  estimating network traffic demand: needed to determine how much bandwidth is “enough” (for that much traffic)

## Slide 7: Providing multiple classes of service
thus far: making the best of best effort service
  one-size fits all service model
alternative: multiple classes of service
  partition traffic into classes
  network treats different classes of traffic differently (analogy: VIP service versus regular service)
0111
granularity: differential service among multiple classes, not among individual connections
history: ToS bits

## Slide 8: Multiple classes of service: scenario
R1
R2
H1
H2
H3
H4
1.5 Mbps link
R1 output
interface
queue

## Slide 9: Scenario 1: mixed HTTP and VoIP
example: 1Mbps VoIP, HTTP share 1.5 Mbps link.
  HTTP bursts can congest router, cause audio loss
  want to give priority to audio over HTTP
packet marking needed for router to distinguish between different classes; and new router policy to treat packets accordingly
Principle 1
R1
R2

## Slide 10: Principles for QOS guarantees (more)
what if applications misbehave (VoIP sends higher than declared rate)
  policing: force source adherence to bandwidth allocations
marking, policing at network edge
provide protection (isolation) for one class from others
Principle 2
R1
R2
1.5 Mbps link
1 Mbps
phone
packet marking and policing

## Slide 11: Principles for QOS guarantees (more)
allocating fixed (non-sharable) bandwidth to flow: inefficient use of bandwidth if flows doesn’t use its allocation
while providing isolation, it is desirable to use
resources as efficiently as possible
Principle 3
R1
R2
1.5 Mbps link
1 Mbps
phone
1 Mbps logical link
0.5 Mbps logical link

## Slide 12: Review: Queues on routers
Where does contention between the two connections happen in the network earlier?
  Contention == increased queueing (and queuing delays), possibility of loss
Where are the queues located on the routers?
Principle: It is useful to provide quality of service by managing how packets traverse router queues, ie: packet scheduling

## Slide 13: Packet scheduling for QoS
Shaping and policing

## Slide 14: Review: Packet scheduling for QoS
packet scheduling: choose next queued packet to send on outgoing link
previously covered under the networking layer
  FCFS: first come first served
  simply multi-class priority
  round robin
  weighted fair queueing (WFQ)
queue
(waiting area)
packet
arrivals
packet
departures
link
(server)

## Slide 15: Packet scheduling mechanisms
Goal: provide isolation between different kinds of traffic by limiting traffic not to exceed declared parameters
Three commonly used criteria:
(long term) average rate: how many pkts can be sent per unit time (in the long run)
  crucial question: what is the interval length: 100 packets per sec or 6000 packets per min have same average!
peak rate: e.g., 6000 pkts per min (ppm) avg.; 1500 ppm peak rate
(max.) burst size: max number of pkts sent consecutively (with no intervening idle)

## Slide 16: QoS mechanism (1): Leaky Bucket
Used in conjunction with resource reservation to police the host’s reservation
At the host-network interface, allow packets into the network at a constant rate
Packets may be generated in a bursty manner, but after they pass through the leaky bucket, they enter the network evenly spaced

## Slide 17: Leaky Bucket: Analogy
Leaky
Bucket
Network
Packets from host

## Slide 18: Shaping traffic with leaky buckets
The leaky bucket is a traffic shaper: It changes the characteristics of packet stream
Traffic shaping makes traffic more manageable and more predictable
Usually, a system/network administrator would set the rate at which packets may be sent through the leaky bucket
Administrator also sets up policies to map any connection that started up to a leaky bucket (and rate) of its own

## Slide 19: Issues with a leaky bucket
In some cases, we may want to allow short bursts of packets to enter the network without smoothing them out
For a leaky bucket, average rate == peak rate
But sometimes, we can allow the peak rate to be higher
  Ex: a short transfer that only has a few packets
For this purpose we use a token bucket, which is an enhanced leaky bucket

## Slide 20: QoS mechanism (2): Token Bucket
token bucket: limit input to specified burst size and average rate
bucket can hold b tokens
tokens generated at rate r tokens/sec unless bucket full
over interval of length t: number of packets admitted less than or equal to (r * t + b)

## Slide 21: Token Bucket: Notes
The bucket holds tokens instead of packets
Tokens are generated and placed into the token bucket at a constant rate
When a packet arrives at the token bucket, it is transmitted if there is a token available.
Otherwise it may be buffered until a token becomes available
  Or even dropped: in which case we call it a policer
  The Internet is full of traffic policers
The token bucket has a fixed size, so when it becomes full, subsequently generated tokens are discarded

## Slide 22: Token Bucket vs. Leaky Bucket
Case 1: Short burst arrivals
6
5
4
3
2
1
0
Arrival time at bucket
Departure time from a leaky bucket
Leaky bucket rate = 1 packet / 2 time units
Leaky bucket size = 4 packets
6
5
4
3
2
1
0
6
5
4
3
2
1
0
Departure time from a token bucket
Token bucket rate = 1 tokens / 2 time units
Token bucket size = 2 tokens

## Slide 23: Token Bucket vs. Leaky Bucket
Case 2: Large burst arrivals
6
5
4
3
2
1
0
Arrival time at bucket
Departure time from a leaky bucket
Leaky bucket rate = 1 packet / 2 time units
Leaky bucket size = 2 packets
6
5
4
3
2
1
0
6
5
4
3
2
1
0
Departure time from a token bucket
Token bucket rate = 1 token / 2 time units
Token bucket size = 2 tokens
??
Departure time from a token bucket policer
Token bucket rate = 1 token / 2 time units
Token bucket size = 2 tokens

## Slide 24: QoS guarantees for delays too!
token bucket, WFQ combine to provide guaranteed upper bound on delay, i.e., QoS guarantee!
WFQ
token rate, r
bucket size, b
per-flow
rate, R
D = b/R
max
arriving
traffic
arriving
traffic

## Slide 25: Differentiated Services
Using marking and packet scheduling to provide QoS

## Slide 26: Differentiated services
want “qualitative” service classes
  “behaves like a wire”
  relative service distinction: Platinum, Gold, Silver
scalability: simple functions in network core, relatively complex functions at edge routers (or hosts)
  signaling, maintaining per-flow router state difficult with large number of flows
don’t define define service classes, provide functional components to build service classes

## Slide 27
Edge-router packet marking
class-based marking: packets of different classes marked differently
intra-class marking: conforming portion of flow marked differently than non-conforming one
profile: pre-negotiated rate r, bucket size b
packet marking at edge based on per-flow profile
possible use of marking:
user packets
rate r
b

## Slide 28: Diffserv architecture
edge router:
per-flow traffic management
marks packets as in-profile and out-profile
core router:
per class traffic management
buffering and scheduling based on marking at edge
preference given to in-profile packets over out-of-profile packets
r
b
marking
scheduling
.
.
.

## Slide 29: Per-connection QoS guarantees
basic fact of life: can not support traffic demands beyond link capacity
call admission: flow declares its needs, network may
block call (e.g., busy signal) if it cannot meet needs
Principle 4
R1
R2
1.5 Mbps link
1 Mbps
phone
1 Mbps
phone

## Slide 30: QoS guarantee scenario
resource reservation
  call setup, signaling (RSVP)
  traffic, QoS declaration
  per-element admission control
  QoS-sensitive scheduling (e.g., WFQ)
request/
reply

## Slide 31: Summary of network support for QoS
Need ways to distinguish traffic (marking) and handle traffic contention (scheduling)
Packet scheduling: a great place to provide QoS by isolating traffic from each other
Abstractions:
  Leaky bucket: shape traffic
  Token bucket: shape and police traffic
The Internet DiffServ architecture builds on these mechanisms
Resource reservation and call admission required to ensure QoS when demand exceeds capacity
  However, not very widely deployed on the Internet today