## Slide 1: Routing Protocols: Part 1
Lecture 23 http://www.cs.rutgers.edu/~sn624/352-S22
Srinivas Narayana

## Slide 2
The network layer is all about reachability.
Every protocol below solves a sub-problem.
DHCP
How does an endpoint get an address?
How does an endpoint talk to another within the same network?
ARP
How does an endpoint talk to another outside its network?
Routing protocols
OSPF, RIP, BGP
Gateways
NAT
Debugging
ICMP
Broadcast
ping
traceroute
Net layer
IPv6

## Slide 3: Review: Key network-layer functions
Forwarding (data plane): move packets from router’s input to appropriate router output
Routing (control plane): determine route taken by packets from source to destination
Analogy: taking a road trip
Forwarding: process of getting through single interchange
Routing: process of planning trip from source to destination
network
layer
runs
everywhere

## Slide 4
How would one design a “Google Maps”
to navigate the Internet?
Routing is a fundamental problem in networking.

## Slide 5: Goals of Routing Protocols #1
Determine good paths from source to destination
“Good” = least cost
  Least propagation delay
  Least cost per unit bandwidth (e.g., $ per Gbit/s)
  Least congested (workload-driven)
“Path” = a sequence of router ports (links)

## Slide 6: Goals of Routing Protocols #2
Make networks resilient to failures
Routers & links can fail without taking down the entire network
Entire subsets can be unreachable; rest still reachable
Hence, the protocol must be distributed

## Slide 7
Routing
Algorithm
data
plane
control
plane
1
2
0111
values in arriving
packet header,
i.e, destination IP address
3
Data plane
per-packet processing, moving packet from input port to output port
Distributed control plane: Components in every router interact with other components to produce a routing outcome.
Per-router control plane
Q1. What info exchanged?
Q2. What computation?
Routing protocol

## Slide 8: The graph abstraction
Routing algorithms work over an abstract representation of a network: the graph abstraction
Each router is a node in a graph
Each link is an edge in the graph
Edges have weights (also called link metrics). Set by netadmin
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
Ex: Rutgers campus
u: Computer Science
v: School of Engineering
…

## Slide 9: The graph abstraction
Routing algorithms work over an abstract representation of a network: the graph abstraction
G = (N, E)
N = {u, v, w, x, y, z}
E = { (u,v), (u,x), (v,x), (v,w), (x,w), (x,y), (w,y), (w,z), (y,z) }
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
Ex: Rutgers campus
u: Computer Science
v: School of Engineering
…

## Slide 10: The graph abstraction
Cost of an edge: c(x, y)
  Examples: c(u, v) = 2, c(u, w) = 5
Cost of a path = sum of edge costs
  c(path x  w  y  z) = 3 + 1 + 2 = 6
Outcome of routing: each node should determine the least cost path to every other node
Q1: What information should nodes exchange with each other to enable this computation?
Q2: What algorithm should each node run to compute the least cost path to every node?
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5

## Slide 11: The rest of this lecture
Routing protocols
Link state
protocols
Distance vector protocols
Each router has complete information of the graph
Messages exchanged by flooding all over the network
Communication expensive, but complete
Each router only maintains distances & next hop to others
Messages are exchanged over each link and stay within the link
Communication cheap, but incomplete

## Slide 12: Link State Protocols

## Slide 13: Link state protocol
Each router knows the state of all the links and routers in the network
Every router performs an independent computation on globally shared knowledge of network’s complete graph representation
Distance vector protocols
Routing protocols
Link state
protocols

## Slide 14: Q1: Information exchange
Link state flooding: the process by which neighborhood information of each network router is transmitted to all other routers
Each router sends a link state advertisement (LSA) to each of its neighbors
LSA contains the router ID, the IP prefix owned by the router, the router’s neighbors, and link cost to those neighbors
Upon receiving an LSA, a router forwards it to each of its neighbors: flooding
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5

## Slide 15: Q1: Information exchange
Eventually, the entire network receives LSAs originated by each router
LSAs put into a link state database
LSAs occur periodically and whenever the graph changes
  Example: if a link fails
  Example: if a new link or router is added
The routing algorithm running at each router can use the entire network’s graph to compute least cost paths
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5

## Slide 16: Q2: The algorithm
Dijkstra’s algorithm
Given a network graph, the algorithm computes the least cost paths from one node (source) to all other nodes
This can then be used to compute the forwarding table at that node
Iterative algorithm: maintain estimates of least costs to reach every other node. After k iterations, each node definitively knows the least cost path to k destinations
Notation:
c(x,y): link cost from node x to y; = ∞ if not direct neighbors
D(v): current estimate of cost of path from source to destination v
p(v): (predecessor node) the last node before v on the path from source to v
N': set of nodes whose least cost path is definitively known

## Slide 17: Dijsktra’s Algorithm
1 Initialization:
2 N' = {u}
3 for all nodes v
4 if v adjacent to u
5 then D(v) = c(u,v)
6 else D(v) = ∞
7
8 Loop
9 find w not in N' such that D(w) is a minimum
10 add w to N'
11 update D(v) for all v adjacent to w and not in N' :
12 D(v) = min( D(v), D(w) + c(w,v) )
13 /* new cost to v is either old cost to v or known
14 shortest path cost to w plus cost from w to v */
15 until all nodes in N'
Initial estimates of distances are just the link costs of neighbors.
Least cost node among all estimates. This cost cannot decrease further.
Relaxation

## Slide 18: Visualization
v
w
u
N’
nodes whose least cost paths from u are definitively known
v’
v’’
N \ N’
Nodes with estimated least path costs, not definitively known to be smallest possible
min cost in N \ N’
D(w)
c(w, v)
D(v)
W should move to N’.
Relaxation: for each v in N \ N’, is the cost of the path via w smaller than known least cost path to v?
If so, update D(v)
Predecessor of v is w.
Cost of path via w: D(w) + c(w,v)
Cost of known best path: D(v)

## Slide 19: Dijkstra’s algorithm: example
Step
0
1
2
3
4
5
N'
u
ux
uxy
uxyv
uxyvw
uxyvwz
D(v),p(v)
2,u
2,u
2,u
D(w),p(w)
5,u
4,x
3,y
3,y
D(x),p(x)
1,u
D(y),p(y)
∞
2,x
D(z),p(z)
∞
∞
4,y
4,y
4,y
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5

## Slide 20: Constructing the forwarding table
To find the router port to use for a given destination (router), find the predecessor of the node iteratively until reaching an immediate neighbor of the source u
The port connecting u to this neighbor is the output port for this destination

## Slide 21: Constructing the forwarding table
Suppose we want forwarding entry for z.
D(v),p(v)
2,u
D(w),p(w)
3,y
D(x),p(x)
1,u
D(y),p(y)
2,x
D(z),p(z)
4,y
z: p(z) = y
y: p(y) = x
x: p(x) = u
x is an immediate
neighbor of u
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
z
(u,x)
destination
link
Forwarding table at u:

## Slide 22: Summary of link state protocols
Each router announces link state to the entire network using flooding
Each node independently computes least cost paths to every other node using the full network graph
Dijkstra’s algorithm can efficiently compute these best paths
  Easy to populate the forwarding table from predecessor information computed during the algorithm

## Slide 23: Distance Vector Protocols

## Slide 24: Distance Vector Protocol
Each router only exchanges a distance vector with its neighbors
  Distance: how far the destination is
  Vector: a value for each destination
DVs are only exchanged between neighbors; not flooded
Use incomplete view of graph derived from neighbors’ distance vectors to compute the shortest paths
Distance vector protocols
Routing protocols
Link state
protocols

## Slide 25: Q1: Distance Vectors
Dx(y) = estimate of least cost from x to y
Distance vector: Dx = [Dx(y): y є N ]
Node x knows cost of edge to each neighbor v: c(x,v)
Node x maintains Dx
Node x also maintains its neighbors’ distance vectors
  For each neighbor v, x maintains Dv = [Dv(y): y є N ]
Nodes exchange distance vector periodically and whenever the local distance vector changes (e.g., link failure, cost changes)
Notes: At each node we need
- an array (known as DV) that lists the current least costs to reach all known destinations
- also need to maintain the next-hop along the least cost path
- the DV’s from all neighbors

## Slide 26: Q2: Algorithm
Bellman-Ford algorithm
Each node initializes its own distance vector (DV) to edge costs
Each node sends its DVs to its neighbors
When a node x receives new DV from a neighbor v, it updates its own DV using the Bellman-Ford equation:
Given dx(y) := estimated cost of the least-cost path from x to y
Update dx(y) = minv {c(x,v) + dv(y) }
cost to reach neighbor v directly from x
minimum taken over
all neighbors v of x
cost of path from neighbor v to destination y

## Slide 27: Visualization
Which neighbor v offers the current best path from x to y?
Path through neighbor v has cost c(x,v) + dv(y)
Choose min-cost neighbor
Remember min-cost neighbor as the one used to reach node y
This neighbor determines the output port!
x
v
y
c(x,v)
Neighbor v sends its distance vector to x.
dv(y)
v’
v’’
v’’’
Use v’’ and link (x,v’’) to reach y.

## Slide 28
x y z
x
y
z
0 2 7
∞
∞
∞
∞
∞
∞
from
cost to
from
from
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
∞
∞
∞
∞
∞
cost to
x y z
x
y
z
0 2 7
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 7
from
cost to
x y z
x
y
z
∞
∞
∞
7
1
0
cost to
2 0 1
∞ ∞ ∞
2 0 1
7 1 0
2 0 1
7 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
time
x
z
1
2
7
y
node x table
node y table
node z table
Dx(y) = min{c(x,y) + Dy(y), c(x,z) + Dz(y)} = min{2+0 , 7+1} = 2
Dx(z) = min{c(x,y) + Dy(z),
c(x,z) + Dz(z)}
= min{2+1 , 7+0} = 3
∞
Notes: This example assumes that nodes are computing routes in a lock-step fashion.

## Slide 29: Good news travels fast
Suppose the link cost reduces or a new better path becomes available in a network.
The immediate neighbors of the change detect the better path immediately
Since their DV changed, these nodes notify their neighbors immediately.
  And those neighbors notify still more neighbors
  … until the entire network knows to use the better path
Good news travels fast through the network
This is despite messages only being exchanged among neighbors
x
z
1
4
2
y
1

## Slide 30: Bad news travels slowly
If router goes down, could be a while before network realizes it.
A
B
C
D
E
1
2
3
4
3
2
3
4
3
4
3
4
5
4
5
4
5
6
5
6
7
6
7
6
Initially
After 1 exchange
After 2 exchanges
After 3 exchanges
After 4 exchanges
After 5 exchanges
etc… to infinity
Count to infinity problem
B still thinks it can reach A through C… bad!
C thinks it can reach A through B… worse!
B, D think they can reach A through C… ugly!

## Slide 31: Bad news travels slowly
Reacting appropriately to bad news requires information that only other routers have. DV does not exchange sufficient info.
B needs to know that C has no other path to A other than via B.
DV does not exchange paths; just distances!
Poisoned reverse: if X gets its route to Y via Z, then X will announce dX(Y) = ∞ in its message to Z
  Effect: Z won’t use X to route to Y
  However, this won’t solve the problem in general (think why.)
A
B
C
D
E

## Slide 32: Summary: Comparison of LS and DV
Link State Algorithms
Nodes have full visibility into the network’s graph
Copious message exchange: each LSA is flooded over the whole network
Robust to network changes and failures
Distance Vector Algorithms
Only distances and neighbors are visible
Sparse message exchange: DVs are exchanged among neighbors only
Brittle to router failures. Incorrect info may propagate all over net
OSPF
Open Shortest Path First
(v2 RFC 2328)
EIGRP
Enhanced Interior Gateway Routing Protocol
(RFC 7868)