## Slide 1
Transport

## Slide 2: Review: slow start, additive inc
1K
Time
Packet drops/
RTO
Slow start
Slow start
Congestion Window
Say MSS = 1 KByte
Default ssthresh = 64KB = 64 MSS
54 MSS
Set ssthresh to
27 MSS
Loss occurs at cwnd = 40K
Loss occurs at cwnd = 54K
Set ssthresh to
20 MSS
Additive increase
Slow
start
Additive increase
AI is slow.
Persistent connections
Large window sizes
Different laws to evolve congestion window

## Slide 3: The components of delay
Increasing time
Transmission delay at the first link
Propagation delay of first link
Queueing at the router
Propagation delay of second link
Transmission delay at the second link

## Slide 4: Bandwidth-Delay Product

## Slide 5: Steady state cwnd for a single flow
Suppose the bottleneck link has rate C
Suppose the propagation round-trip delay (propRTT) between sender and receiver is T
Ignore transmission delays for this example;
Assume steady state: highest sending rate with no bottleneck congestion
Q: how much data is in flight over a single RTT?
C * T data i.e., amount of data unACKed at any point in time
ACKs take time T to arrive (without any queueing). In the meantime, sender is transmitting at rate C

## Slide 6: The Bandwidth-Delay Product
C * T = bandwidth-delay product:
  The amount of data in flight for a sender transmitting at the ideal rate during the ideal round-trip delay of a packet
Note: this is just the amount of data “on the pipe”
Data
C * T

## Slide 7: The Bandwidth-Delay Product
Q: What happens if cwnd > C * T?
  i.e., where are the rest of the in-flight packets?
A: Waiting at the bottleneck router queues
Data
C * T

## Slide 8: Router buffers and the max cwnd
Router buffer memory is finite: queues can only be so long
  If the router buffer size is B, there is at most B data waiting in the queue
If cwnd increases beyond C * T + B, data is dropped!
Data
C * T
B

## Slide 9: BDP is a crucial value for a flow
Bandwidth-Delay Product (BDP) governs the window size of a single flow at steady state
The bottleneck router buffer size governs how much the cwnd can exceed the BDP before packet drops occur
BDP is the ideal desired window size to use the full bottleneck link, without any queueing.
  Accommodating flow control, also the min socket buffer size to use the bottleneck link fully

## Slide 10: Demo of the impact of BDP & B
Utilization
Congestion window

## Slide 11: Detecting and Reacting Better to Packet Loss

## Slide 12: Can we detect loss earlier than RTO?
Key idea: use the information in the ACKs. How?
Suppose successive (cumulative) ACKs contain the same ACK#
  Also called duplicate ACKs
  Occur when network is reordering packets, or one (but not most) packets in the window were lost
  Fast retransmit: (1) Immediately retransmit packet
Reduce cwnd when you see many duplicate ACKs
  Consider many dup ACKs a strong indication that packet was lost
  Default threshold: 3 dup ACKs, i.e., triple duplicate ACK
  Make cwnd reduction gentler than setting cwnd = 1; recover faster
  Fast retransmit: (2) reduce window to half of its current value

## Slide 13: Additive Increase/Multiplicative Decrease
1K
Time
Triple duplicate ACK
Slow start
In-flight data
Say MSS = 1 KByte
Default ssthresh = 64KB = 64 MSS
Switch to additive increase at cwnd = ssthresh = 64K
Perceived loss occurs at cwnd = 80K
(2) Set inflight = ssthresh = 40K
Additive increase
Additive increase
Fast retransmit: (1) retransmit dup-ACKed segment
Fast recovery keeps inflight stable until new ACK
New ACK
RTO
RTO: window drops all the way to 1 MSS
(2) Multiplicative decrease

## Slide 14
TCP New Reno performs additive increase and multiplicative decrease of congestion window.
In short, we often refer to this as AIMD.
Multiplicative decrease is a part of all TCP algorithms. It is necessary for fairness across TCP flows.

## Slide 15: Why does multiplicative decrease help?
Efficiency and Fairness
Chiu and Jain, “Increase and decrease algorithms for congestion avoidance”

## Slide 16: Efficient allocation
Don’t want sources to transmit either too slow or too fast
  Slow: Underutilize the network
  Fast: High delays, lose packets
Every endpoint is reacting
  May all under/overshoot
  Large oscillations possible!
Optimal efficiency:
  xi = Xgoal e.g., link capacity
Efficiency = 1 - distance from efficiency line
User 1: x1
User 2: x2
Efficiency
line
2 user example
overload
underload

## Slide 17: Fair allocation
Max-min fairness
Flows which share the same bottleneck get the same amount of bandwidth
Fairness = 1 - distance from fairness line
User 1: x1
User 2: x2
2 user example
2 getting
too much
1 getting
too much
fairness
line

## Slide 18: How should transports react?
Given efficiency and fairness goals above, how should transports behave?
Consider x(t), window or rate of a source, evolving over time t
Assume discrete time steps.
x(t + 1) = function of x(t), feedback from the network

## Slide 19: Linear control rules
xi(t): window or rate of the ith user at time t
aI, aD, bI, bD: constant increase/decrease coefficients
Assumption: All users receive same network feedback
  Binary feedback: sense congestion or available capacity
Assumption: All users increase or decrease simultaneously

## Slide 20: Additive increase, multiplicative decrease
(bDx1+aI, bDx2+aI)
User 1: x1
User 2: x2
fairness
line
efficiency
line
(x1,x2)
(bDx1,bDx2)
bI = 1, aD = 0
Multiplicative decrease enables converging to fairness
Oscillates around the most efficient point

## Slide 21: Convergent doesn’t mean static