## Slide 1
Network
Ack: Slides heavily adapted from Jen Rexford and Michael Schapira

## Slide 2
Routing
Algorithm
data
plane
control
plane
1
2
0111
values in arriving
packet header,
i.e, destination IP address
3
Data plane
per-packet processing, moving packet from input port to output port
Distributed control plane: Components in every router interact with other components to produce a routing outcome.
Per-router control plane

## Slide 3: So far
What outcome is computed? Spanning tree, shortest paths, …
What algorithm is used?
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
1
2
3
4
5
6
7
Q1. What info exchanged?
Q2. What computation?
Routing protocol

## Slide 4: Internet Routing

## Slide 5: The Internet is a large federated network
AT&T
Comcast
Verizon

## Slide 6: The Internet is a large federated network
AT&T
Comcast
Verizon
Several autonomously run organizations: No one “boss”
Organizations cooperate, but also compete
e.g., AT&T has little commercial interest in revealing its internal network structure to Verizon.

## Slide 7: The Internet is a large federated network
AT&T
Comcast
Verizon
Several autonomously run organizations: No one “boss”
Organizations cooperate, but also compete
Message exchanges must
not reveal internal network details.
Algorithm must work with “incomplete” information about its neighbors’ internal topology.

## Slide 8: The Internet is a large federated network
AT&T
Comcast
Verizon
Internet today: > 70,000 unique autonomous networks
Internet routers: > 800,000 forwarding table entries
Keep messages & tables as small as possible. Don’t flood
Algorithm must be incremental: don’t recompute the whole table on every message exchanged.

## Slide 9: Local Control vs. Global Properties
The Internet is a “network of networks”
  ~35,000 separately administered networks
  Competitive cooperation for e2e reachability
Local Control
Intradomain routing,
interdomain policies
Global Properties
Performance, security, reliability, scalability

## Slide 10: Two-Tiered Routing Architecture
Goal: distributed management of resources
  Internetworking of multiple networks
  Networks under separate administrative control
Intradomain: inside a region of control
  Routers configured to achieve a common goal
  Okay for routers to share topology information
  Different ASes can run different protocols
Interdomain: between regions of control
  ASes have different (maybe conflicting) goals
  Routers only share reachability information

## Slide 11: Internet Structure

## Slide 12: Autonomous Systems (ASes)
AS-level topology
  Nodes are Autonomous Systems (ASes)
  Destinations are prefixes (e.g., 12.0.0.0/8)
  Edges are links and business relationships
1
2
3
4
5
6
7
Client
Web server

## Slide 13: AS Numbers (ASNs)
ASNs are 16 bit values (or 32-bit).
64512 through 65535 are “private”
Level 3: 1
MIT: 3
Harvard: 11
Rutgers:
Princeton: 88
AT&T: 7018, 6341, 5074, …
Verizon: 701, 702, 284, 12199, …
Sprint: 1239, 1240, 6211, 6242, …
…
Currently > 70,000 in use.

## Slide 14: Business Relationships Between ASes
Neighboring ASes have business contracts
  How much traffic to carry
  Which destinations to reach
  How much money to pay
Common business relationships
  Customer-provider
  Peer-peer

## Slide 15: Customer-Provider Relationship
Customer needs to be reachable from everyone
  Provider ensures all neighbors can reach the customer
  Customer “default-routes” to provider
Customer does not want to provide transit service
  Customer does not let its providers send traffic through it
d
d
provider
customer
customer
provider
Traffic to the customer
Traffic from the customer
traffic

## Slide 16: Peer-Peer Relationship
Peers exchange traffic between customers
  AS lets its peer reach (only) its customers
  AS can reach its peer’s customers
  Often the relationship is settlement-free (i.e., no $$$)
peer
peer
Traffic to/from the peer and its customers
d
traffic

## Slide 17: AS Structure: Tier-1 Providers
Top of the Internet hierarchy
  Has no upstream provider of its own, no default routes
  Typically has a large (inter)national backbone
  Around 10-12 ASes: AT&T, Sprint, Level 3, …
peer-peer
peer-peer
peer-peer
peer-peer
Notes: Fully connect to each other so they can reach each other’s customers.

## Slide 18: AS Structure: Other ASes
Lower-layer providers (tier-2, …)
  Provide transit service to downstream customers
    But need at least one provider of their own
  Typically have national or regional scope
    E.g., Minnesota Regional Network
Stub ASes
  Do not provide transit service
  Connect to upstream provider(s)
  Most ASes (e.g., 85-90%)
  E.g., Princeton, Rutgers, …

## Slide 19: Policy-Based Path-Vector Routing

## Slide 20: Shortest-Path Routing is Restrictive
All traffic must travel on shortest paths
All nodes need common notion of link costs
Incompatible with commercial relationships
Regional
ISP1
Regional
ISP2
Regional
ISP3
Cust1
Cust3
Cust2
National
ISP1
National
ISP2
YES
NO

## Slide 21: Path-Vector Routing
Extension of distance-vector routing
  Support flexible routing policies
  Faster convergence(avoid count-to-infinity)
Key idea: advertise the entire path
  Distance vector: send distance metric per dest d
  Path vector: send the entire path for each dest d
3
2
1
d
“d: path (2,1)”
“d: path (1)”
data traffic
data traffic

## Slide 22: Faster Loop Detection
Node can easily detect a loop
  Look for its own node identifier in the path
  E.g., node 1 sees itself in the path “3, 2, 1”
Node can simply discard paths with loops
  E.g., node 1 simply discards the advertisement
3
2
1
“d: path (2,1)”
“d: path (1)”
“d: path (3,2,1)”

## Slide 23: Flexible Policies
Each node can apply local policies
  Path selection: Which path to use?
  Path export: Whether to advertise the path?
Examples
  Node 2 may prefer the path “2, 3, 1” over “2, 1”
  Node 1 may not let node 3 hear the path “1, 2”
2
3
1
2
3
1

## Slide 24: Border Gateway Protocol

## Slide 25: Border Gateway Protocol
IP-Prefix-based path-vector protocol
Policy-based routing based on AS Paths
Evolved during the past 40 years
1989 : BGP-1 [RFC 1105], replacement for EGP
1990 : BGP-2 [RFC 1163]
1991 : BGP-3 [RFC 1267]
1995 : BGP-4 [RFC 1771], support for CIDR
2006 : BGP-4 [RFC 4271], update
“BGP at 18”: http://www.youtube.com/watch?v=HAOVNYSnL7k

## Slide 26: BGP Operations
Establish session on
TCP port 179
Exchange all
active routes
Exchange incremental
updates
AS1
AS2
While connection
is ALIVE exchange
route UPDATE messages
BGP session

## Slide 27: Incremental Protocol
A node learns multiple paths to destination
  Stores all of the routes in a routing table (RIB)
  Applies policy to select a single active route (FIB)
  … and may advertise the route to its neighbors
Incremental updates
  Announcement
    Upon selecting a new active route, add node id to path
    … and (optionally) advertise to each neighbor
  Withdrawal
    If the active route is no longer available
    … send a withdrawal message to the neighbors

## Slide 28: BGP Route
Destination prefix (e.g., 128.112.0.0/16)
Route attributes, including
  AS path (e.g., “7018 88”)
  Next-hop IP address (e.g., 12.127.0.121)
AS 88
Princeton
128.112.0.0/16
AS path = 88
Next Hop = 192.0.2.1
AS 7018
AT&T
AS 11
Yale
192.0.2.1
128.112.0.0/16
AS path = 7018 88
Next Hop = 12.127.0.121
12.127.0.121
128.112.0.0/16

## Slide 29: BGP Path Selection
Simplest case
  Shortest AS path
  Arbitrary tie break
Example
  Three-hop AS path preferred over a five-hop AS path
  AS 12654 prefers path through Global Crossing
But, BGP is not limited to shortest-path routing
  Policy-based routing
AS 3549
Global Crossing
128.112.0.0/16
AS Path = 3549 7018 88
AS 12654
RIPE NCC
RIS project
AS 1129
Global Access
128.112.0.0/16
AS Path = 1129 1755 1239 7018 88

## Slide 30: BGP Policy: Influencing Decisions
Best Route
Selection
Apply Import
Policies
Best Route
Table
Apply Export
Policies
Install forwarding
Entries for best
Routes.
Receive
BGP
Updates
Best
Routes
Transmit
BGP
Updates
Apply Policy =
filter routes &
tweak attributes
Based on
Attribute
Values
IP Forwarding Table
Apply Policy =
filter routes &
tweak attributes
Open ended programming.
Constrained only by vendor configuration language

## Slide 31: BGP Policy: Applying Policy to Routes
Import policy
  Filter unwanted routes from neighbor
    E.g. prefix that your customer doesn’t own
  Manipulate attributes to influence path selection
    E.g., assign local preference to favored routes
Export policy
  Filter routes you don’t want to tell your neighbor
    E.g., don’t tell a peer a route learned from other peer
  Manipulate attributes to control what they see
    E.g., make a path look artificially longer than it is

## Slide 32: BGP Policy Examples

## Slide 33: Import Policy: Local Preference
Favor one path over another
  Override the influence of AS path length
  Apply local policies to prefer a path
Example: prefer customer over peer
AT&T
Sprint
Yale
Tier-2
Tier-3
Local-pref = 100
Local-pref = 90

## Slide 34: Import Policy: Filtering
Discard some route announcements
  Detect configuration mistakes and attacks
Examples on session to a customer
  Discard route if customer doesn’t own the prefix
  Discard route containing other large ISPs
Patriot
Princeton
USLEC
128.112.0.0/16

## Slide 35: Export Policy: Filtering
Discard some route announcements
  Limit propagation of routing information
Examples
  Don’t announce routes from one peer to another
AT&T
Sprint
UUNET

## Slide 36: Export Policy: Filtering
Discard some route announcements
  Limit propagation of routing information
Examples
  Don’t announce routes for network-management hosts or the underlying routers themselves
USLEC
Princeton
network operator

## Slide 37: Export Policy: Attribute Manipulation
Modify attributes of the active route
  To influence the way other ASes behave
Example: AS prepending
  Artificially inflate AS path length seen by others
  Convince some ASes to send traffic another way
Patriot
Princeton
USLEC
128.112.0.0/16
Sprint
88 88
88

## Slide 38: BGP Policy Configuration
Policy languages are vendor-specific
  Not part of the BGP protocol specification
  Different languages for Cisco, Juniper, etc.
Still, all languages have some key features
  Policy as a list of clauses
  Each clause matches on route attributes
  … and discards or modifies the matching routes
Configuration done by human operators
  Implementing the policies of their AS
  Biz relationships, traffic engineering, security, …

## Slide 39: BGP Inside an AS

## Slide 40: An AS is Not a Single Router
Multiple routers in an AS
  Need to distribute BGP information within the AS
  Internal BGP (iBGP) sessions between routers
AS1
AS2
eBGP
iBGP

## Slide 41: Internal BGP and Local Preference
Example
  Both routers prefer the path through AS 100 on the left
  … even though the right router learns a different external path
I-BGP
AS 256
AS 300
Local Pref = 100
Local Pref = 90
AS 100
AS 200

## Slide 42: Joining BGP and IGP Information
Border Gateway Protocol (BGP)
  Announces reachability to external destinations
  Maps a destination prefix to an egress point
    128.112.0.0/16 reached via 192.0.2.1
Interior Gateway Protocol (IGP)
  Used to compute paths within the AS
  Maps an egress point to an outgoing link
    192.0.2.1 reached via 10.1.1.1
192.0.2.1
10.1.1.1

## Slide 43: An AS May Learn Many Routes
Multiple connections to neighboring ASes
  Multiple border routers may learn good routes
  … with the same local-pref and AS path length
1
2
3
4
5
6
7
Multiple links

## Slide 44: Hot-Potato (Early-Exit) Routing
Hot-potato routing
  Each router selects the closest egress point
  … based on the path cost in intradomain protocol
BGP decision process
  Highest local preference
  Shortest AS path
  Closest egress point
  Arbitrary tie break
hot potato
A
B
C
D
G
E
F
4
5
3
9
3
4
10
8
8
A
B
dst

## Slide 45: Learning the locations of the endpoints

## Slide 46: Finding the endpoints
Computing the forwarding table
  Still must figure out where the endpoints are
How to find the endpoints?
  Learning/flooding (Ethernet)
  Injecting into the routing protocol
  Dissemination using a different protocol
  Central directory service
Ways to curb scaling challenges
  E.g., spanning tree per VLAN for endpoint flooding

## Slide 47: Learning and Flooding
When a frame arrives
  Inspect the source address
  Associate address with the incoming interface
When the frame has an unfamiliar destination
  Forward out all interfaces
  … except for the one where the frame arrived
A
B
C
D
Switch learns how to reach A.
A
B
C
D
When in doubt, shout!
Used in Ethernet LANs

## Slide 48: Inject into Routing Protocol
Treat the end host (or subnet) as a node
  And disseminate in the routing protocol
  E.g., flood information about where addresses attach
3
2
2
1
1
4
1
4
5
3
u
s
6
Used in OSPF and IS-IS, especially in enterprise networks
. . .

## Slide 49: Disseminate with another protocol
One router learns the route
… and shares the information with other routers
learn a route to d
(e.g., via BGP)
disseminate route to other routers
Internal BGP (iBGP) used in backbone networks

## Slide 50: Directory Service
Contact a service to learn the location
  Lookup the end-host or subnet address
  … and learn the label to put on the packet
  … to get the traffic to the right egress point
s
d
i
e
directory
“Host d is at egress e”
Encapsulate packet to send to egress e.
Used in some data centers.

## Slide 51: Conclusion
Routing is a distributed computation
  With challenges in scalability and handling dynamics
Different solutions for different environments
  Ethernet LAN: spanning tree, MAC learning, flooding
  Enterprise: link-state routing, injecting subnet addresses
  Backbone: link-state routing inside, path-vector routing with neighboring domains, and iBGP dissemination
  Internet: BGP
  Data centers: many different solutions, still in flux
    An active research area…