## Slide 1: Internet and Web Architecture
A review
Lecture 2
Srinivas Narayana
http://www.cs.rutgers.edu/~sn624/553-S23

## Slide 2: Outline
Name resolution
The HTTP protocol
Socket abstraction
Underlying transport concerns: reliability, basic congestion control
Internet routing: IP address organization, BGP, and concerns
CDN reading : Tom Leighton, Akamai full detailed study
Relevant points from Google, FB, Microsoft edge and peering papers
HTTP/TCP interaction?

## Slide 3: Software/hardware organization at hosts
Link: best-effort local pkt delivery
Network: best-effort global pkt delivery
Transport: provide guarantees to apps
Application: useful user-level functions
Communication functions broken up and “stacked”
Each layer depends on the one below it.
Each layer supports the one above it.
The interfaces between layers are well-defined and standardized.

## Slide 4
Link layer
Network
Transport
Applications
Link layer
Network
Transport
Applications
The Internet
Packet takes on headers (metadata) at each layer
Packet starts as an
app “payload”

## Slide 5: Name Resolution

## Slide 6
Google
google.com
Machines communicate using IP addresses and ports
IP addresses: ~12 digits (IPv4) or more
Ports: fixed based on application (e.g., 80: web)
Need a way to turn human-readable addresses into Internet addresses.
Ask someone
Ask everyone
Tell everyone
Directory service
Query broadcast
Information flooding
Asking “someone” could involve asking many machines…

## Slide 7: Domain Name Service
Key idea: Implement a server that looks up a table.
Will this scale?
  Every new (changed) host needs to be (re)entered in this table
  Performance: can the server serve billions of Internet users?
  Failure: what if the server or the database crashes?
  Security: What if someone “takes over” this server?
DOMAIN NAME | IP ADDRESS
spotify.com | 98.138.253.109
cs.rutgers.edu | 128.6.4.2
www.google.com | 74.125.225.243
www.princeton.edu | 128.112.132.86
QUERY cs.rutgers.edu
RESPONSE 128.6.4.2
<Client IP, CPort, DNS server IP, 53>
<DNS server, 53, Client IP, Cport>

## Slide 8: Distributed and hierarchical database
Root DNS Servers
com DNS servers
org DNS servers
edu DNS servers
rutgers.edu
DNS servers
umass.edu
DNS servers
google.com
DNS servers
amazon.com
DNS servers
wnyc.org
DNS servers
cs.rutgers.edu DNS server
RFC 1034
Top-level domain (TLD) servers
Authoritative name server
Hierarchy
Replication
Indirection

## Slide 9: DNS name resolution
requesting host
cs.rutgers.edu
gaia.cs.umass.edu
root DNS server
local DNS server
dns.rutgers.edu
1
2
3
4
5
6
umass.edu DNS server
dns.umass.edu
7
8
.edu DNS server
Host at cs.rutgers.edu wants IP address for gaia.cs.umass.edu
Local DNS server
Root DNS server
TLD DNS server
Authoritative DNS server

## Slide 10: DNS caching
requesting host
cs.rutgers.edu
gaia.cs.umass.edu
root DNS server
local DNS server
dns.rutgers.edu
1
2
3
4
5
6
umass.edu DNS server
dns.umass.edu
7
8
.edu DNS server
Once (any) name server learns a name to IP address mapping, it caches the mapping
Cache entries timeout (disappear) after some time
TLD servers typically cached in local name servers
In practice, root name servers aren’t visited often!
Caching is pervasive in DNS

## Slide 11: Example DNS interactions
dig <domain-name>
dig +trace <domain-name>
dig @<dns-server> <domain-name>

## Slide 12
Google
google.com
The web is a specific application protocol running over a network: HyperText Transfer Protocol (HTTP)
Objects
Each object addressable by a name (URL)
Named objects can be static (image, video)
… or the result of a dynamic app process

## Slide 13: Web interactions
Hostname | IP address
Google.com | 10.0.1.2
Host name
Server IP Address
DNS server
clientIP, clientPort, server IP Address, 80
HTTP messages
(HTTP application typically associated with port 80)
HTTP request
HTTP response
I want to browse google.com

## Slide 14: Example HTTP interactions
wget google.com (or) curl google.com
telnet example.com 80
  GET / HTTP/1.1
  Host: example.com
(followed by two enter’s)
Exercise: try
  telnet google.com 80
  telnet web.mit.edu 80

## Slide 15: Remembering users: cookies
client
server
http request msg + auth
http response +
Set-cookie: 1678
http request (no auth)
cookie: 1678
Personalized http response
http request (no auth)
cookie: 1678
Personalized http response
cookie-
specific
action
cookie-
specific
action
server
creates ID
1678 for user
entry in backend
database
access
access
Cookie file
Amazon: 1678
Cookie file
Amazon: 1678
Cookie file
Amazon: 1678
one week later:
Netflix: 436
Netflix: 436
Netflix: 436
Cookie is typically opaque to client.

## Slide 16: Improving performance: Web caching
GET foo.html
Web Server
(also called origin server in this context)
Clients
Web cache
GET foo.html
Store foo.html
on receiving response
Network administrators (e.g., Rutgers) may run web caches to remember popular web objects
Hit: cache returns object
Miss: obtain object from originating web server (origin server) and return to client
  Also cache the object locally
Reduce response time
Reduce traffic requirements (and $$) on an organization’s network connections
The Internet
Return cached object!
Rutgers

## Slide 17: Not all content is effectively cacheable
Personalized content
Interactive processing
  e.g., forms, shopping carts, ajax, etc.
Long tail of (obscure) content

## Slide 18: Content Distribution Networks (CDNs)
A global network of web caches
Provisioned by ISPs and network operators
Or content providers, like Netflix, Google, etc.
Uses
Reduce traffic on a network’s Internet connection, e.g., Rutgers
Improve response time for users: CDN nodes are closer to users than origin servers (servers holding original content)
Reduce bandwidth requirements on content provider
Reduce $$ to maintain origin servers

## Slide 19: Without CDN
Problems:
Huge bandwidth requirements for Rutgers
Large propagation delays to reach users
128.6.4.2
DOMAIN NAME | IP ADDRESS
www.yahoo.com | 98.138.253.109
cs.rutgers.edu | 128.6.4.2
www.google.com | 74.125.225.243
www.princeton.edu | 128.112.132.86
Cluster of Rutgers CS origin servers (located in NJ, USA)
DNS
Clients distributed all over the world

## Slide 20: Where the CDN comes in
Distribute content of the origin server over geographically distributed CDN servers
But how will users get to these CDN servers?
Use DNS!
  DNS provides an additional layer of indirection
  Instead of returning IP address, return another DNS server (NS record)
  The second DNS server (run by the CDN) returns IP address to client
The CDN runs its own DNS servers (CDN name servers)
  Custom logic to send users to the “closest” CDN web server

## Slide 21: With CDN
128.6.4.2
DOMAIN NAME | IP ADDRESS
www.yahoo.com | 98.138.253.109
cs.rutgers.edu | 124.8.9.8 (NS record pointing to CDN name server)
www.google.com | 74.125.225.243
DOMAIN NAME | IP ADDRESS
Cs.Rutgers.edu | 12.1.2.3
Cs.Rutgers.edu | 12.1.2.4
Cs.Rutgers.edu | 12.1.2.5
Cs.Rutgers.edu | 12.1.2.6
CDN Name Server (124.8.9.8)
12.1.2.3
12.1.2.4
12.1.2.5
12.1.2.6
Origin server
Client
CDN servers
Custom logic to map ONE domain name to one of many IP addresses!
NS record delegates the choice of IP address to the CDN name server.
Most requests go to CDN servers (caches).
CDN servers may request object from origin
Few client requests go directly to origin server
DNS reply
Popular CDNs:
CloudFlare
Akamai
Level3
…

## Slide 22: Seeing a CDN in action
dig web.mit.edu (or) dig +trace web.mit.edu
telnet web.mit.edu 80

## Slide 23: Application-OS interface

## Slide 24
Google
google.com
Link layer
Network
Transport
Applications
Link layer
Network
Transport
Applications
User
Kernel
Socket
Example: connected socket (TCP)

## Slide 25
Google
google.com
connect(
IPB, portB)
send()
bind(IPaddrB, portB)
listen()
accept()
recv()
process
socket
process
socket
IPA + portA
IPB + portB

## Slide 26
Google
google.com
connect(
IPB, portB)
send()
bind(IPaddrB, portB)
listen()
accept()
recv()

## Slide 27
Google
google.com
Link layer
Network
Transport
Applications
Link layer
Network
Transport
Applications
Socket
User
Kernel

## Slide 28: Transport

## Slide 29: (1) (De)multiplexing
Machine 1
Machine
Machine 1
Machine 1
IP addr 1
IP addr 2
Port 1
Port 2
…
…
…
…
…
Port 65535
socket()
Ports
Src IP, Dst IP,
Tp Protocol
Src port, Dst port
Connection lookup: The operating system does a lookup using these data to determine the right socket and app.
Denotes an attachment point with the network.
Each IP address comes with a full copy of its own ports.
UDP or TCP listening:
(dst IP, dst port, TCP)
TCP established:
(dst IP, dst port, src IP, src port, TCP)

## Slide 30: TCP sockets of different types
Listening (bound but unconnected)
# On server side
ls = socket(AF_INET, SOCK_STREAM)
ls.bind(serv_ip, serv_port)
ls.listen() # no accept() yet
Connected (Established)
# On server side
cs, addr = ls.accept()
# On client side
connect(serv_ip, serv_port)
(src IP, dst IP, src port, dst port)

Socket (cs NOT ls)
(dst IP, dst port)

Socket (ss)
accept() creates a new socket with the
4-tuple (established) mapping
Enables new connections to be demultiplexed correctly
Enables established connections to be demultiplexed correctly

## Slide 31: (2) Reliability: Stop and Wait. 3 Ideas
ACKs: Sender sends a single packet, then waits for an ACK to know the packet was successfully received. Then the sender transmits the next packet.
RTO: If ACK is not received until a timeout, sender retransmits the packet
Seq: Disambiguate duplicate vs. fresh packets using sequence numbers that change on “adjacent” packets
Sender
Receiver
RTT
RTO
SEQ 0
ACK 0
SEQ 1
Retransmit

## Slide 32
Sending one packet per RTT makes the data transfer rate limited by the time between the endpoints, rather than the bandwidth.
Ensure you got the (one) box safely; make N trips
Ensure you get N boxes safely; make just 1 trip!
Keep many packets in flight

## Slide 33: Pipelined reliability
Data in flight: data that has been sent, but sender hasn’t yet received ACKs from the receiver
  Note: can refer to packets in flight or bytes in flight
New packets sent at the same time as older ones still in flight
New packets sent at the same time as ACKs are returning
More data moving in same time!
Improves throughput
  Rate of data transfer

## Slide 34: (3) How much data to keep in flight?
Avoid overwhelming network resources: Congestion control
Internet: every endpoint makes its own decisions!
  Distributed algorithm: no central authority
  Goal 1: efficiency (use available capacity)
  Goal 2: fairness (distribute capacity equitably)
H
C
Feedback Control

## Slide 35: Finding the right congestion window
There is an unknown bottleneck link rate that the sender must match
If sender sends more than the bottleneck link rate:
  packet loss, delays, etc.
If sender sends less than the bottleneck link rate:
  all packets get through; successful ACKs
Congestion window (cwnd): amount of data in flight

## Slide 36: Quickly finding a rate: TCP slow start
Initially cwnd = 1 MSS
  MSS is “maximum segment size”
Upon receiving an ACK of each MSS, increase the cwnd by 1 MSS
Effectively, double cwnd every RTT
Initial rate is slow but ramps up exponentially fast
On loss (RTO), restart from cwnd := 1 MSS
Host A
one segment
RTT
Host B
time
two segments
four segments
Payload
T
N
L
MSS

## Slide 37: Behavior of slow start
1 MSS
Congestion Window
Time
Packet drops/
RTO
Slow start
Slow start
Slow start

## Slide 38: Slow start has problems
Congestion window increases too rapidly
  Example: suppose the “right” window size cwnd is 17
  cwnd would go from 16 to 32 and then dropping down to 1
  Result: massive packet drops
Congestion window decreases too rapidly
  Suppose the right cwnd is 31, and there is a loss when cwnd is 32
  Slow start will resume all the way back from cwnd 1
  Result: unnecessarily low speed of sending data
Instead, perform finer adjustments of cwnd: congestion avoidance

## Slide 39: TCP New Reno: Additive Increase
Remember the recent past to find a good estimate of link rate
The last good cwnd without packet drop is a good indicator
  TCP New Reno calls this the slow start threshold (ssthresh)
Increase cwnd by 1 MSS every RTT after cwnd hits ssthresh
  Effect: increase window additively per RTT
Host A
RTT
Host B
time
four segments
five segments
six segments
RTT
say ssthresh=4
seven segments
…
RTT

## Slide 40: TCP New Reno: Additive increase
Start with ssthresh = 64K bytes (TCP default)
Do slow start until ssthresh
Once the threshold is passed, do additive increase
  Add one MSS to cwnd for each cwnd worth data ACK’ed
  For each MSS ACK’ed, cwnd = cwnd + (MSS * MSS) / cwnd
Upon a TCP timeout (RTO),
  Set cwnd = 1 MSS
  Set ssthresh = max(2 * MSS, 0.5 * cwnd)
  i.e., the next linear increase will start at half the current cwnd

## Slide 41: Behavior of Additive Increase
1K
Time
Packet drops/
RTO
Slow start
Slow start
Congestion Window
Say MSS = 1 KByte
Default ssthresh = 64KB = 64 MSS
54 MSS
Set ssthresh to
27 MSS
Loss occurs at cwnd = 40K
Loss occurs at cwnd = 54K
Set ssthresh to
20 MSS
Additive increase
Slow
start
Additive increase

## Slide 42: Routing

## Slide 43
Google
google.com
Link layer
Network
Transport
Applications
Link layer
Network
Transport
Applications
Socket
User
Kernel
Demultiplexing
Reliability
Congestion control

## Slide 44: Two key network-layer functions
Forwarding: move packets from router’s input to appropriate router output
Routing: determine route taken by packets from source to destination
  routing algorithms
The network layer solves the routing problem.
Analogy: taking a road trip
Forwarding: process of getting through single exit
Routing: process of planning trip from source to destination
network
layer
runs
everywhere

## Slide 45: Control/Data Planes
Data plane = Forwarding
local, per-router function
determines how datagram arriving on router input port is forwarded to router output port
Control plane = Routing
network-wide logic
determines how datagram is routed along end-to-end path from source to destination endpoint
two control-plane approaches:
  Distributed routing algorithm running on each router
  Centralized routing algorithm running on a (logically) centralized machine
0111
values in arriving
packet header
1
2
3

## Slide 46
Routing
Algorithm
data
plane
control
plane
1
2
0111
values in arriving
packet header, i.e, destination IP address
3
Data plane
per-packet processing
(~ tens of nanoseconds)
Control plane
Traditional routing protocols: per route-change processing
(~ a few tens of seconds)
Distributed routing

## Slide 47: The Internet is a large federated network
AT&T
Comcast
Verizon

## Slide 48: The Internet is a large federated network
AT&T
Comcast
Verizon
Several autonomously run organizations (AS’es): No one “boss”
Organizations cooperate, but also compete
e.g., AT&T has little commercial interest in revealing its internal network structure to Verizon.

## Slide 49: The Internet is a large federated network
AT&T
Comcast
Verizon
Several autonomously run organizations: No one “boss”
Organizations cooperate, but also compete
Message exchanges must
not reveal internal network details.
Algorithm must work with “incomplete” information about its neighbors’ internal topology.

## Slide 50: The Internet is a large federated network
AT&T
Comcast
Verizon
Internet today: > 70,000 unique autonomous networks
Internet routers: > 800,000 forwarding table entries
Keep messages & tables as small as possible. Don’t flood
Algorithm must be incremental: don’t recompute the whole table on every message exchanged.

## Slide 51: Inter-domain Routing
The Internet uses Border Gateway Protocol (BGP)
All AS’es speak BGP. It is the glue that holds the Internet together
BGP is a path vector protocol
Distance vector protocols
Routing protocols
Link state
protocols
Path vector protocols
Messages?
Algorithm?
Applicable within a single AS

## Slide 52: (1) BGP Messages
Routing Announcements or Advertisements
  “I am here” or “I can reach here”
  Occur over a TCP connection (BGP session) between routers
Route announcement = destination + attributes
  Destination: IP prefix
Route Attributes:
  AS-level path
  Next hop
  Several others: origin, MED, community, etc.
An AS promises to use advertised path to reach destination
Only route changes are advertised after BGP session established
2b
2d
2c
2a
X
“I am here.”
Dst: 128.1.2.0/24
AS path: X
“I can reach X”
Dst: 128.1.2.0/24
AS path: AS2, X
AS 2
1b
1d
1c
1a
No link metrics, distances!
Exchange paths: path vector
Loop detection is easy
(no “count to infinity”)

## Slide 53: (2) BGP algorithm
A BGP router does not consider every routing advertisement it receives by default to make routing decisions!
  An import policy determines whether a route is even considered a candidate
Once imported, the router performs route selection
A BGP router does not propagate its chosen path to a destination to all other AS’es by default!
  An export policy determines whether a (chosen) path can be advertised to other AS’es and routers
Business policy considerations drive BGP.
NOT efficiency considerations.
Programmed by network operator

## Slide 54: Policy arises from business relationships
Customer-provider relationships:
  E.g., Rutgers is a customer of AT&T
Peer-peer relationships:
  E.g., Verizon is a peer of AT&T
Business relationships depend on where connectivity occurs
  “Where”, also called a “point of presence” (PoP)
  e.g., customers at one PoP but peers at another
  Internet-eXchange Points (IXPs) are large PoPs where ISPs come together to connect with each other (often for free)

## Slide 55: BGP Export Policy
A,B,C are provider networks
X,W,Y are customers (of provider networks)
X is dual-homed: attached to two networks
policy to enforce: X does not want to route from B to C via X
  So, X will not announce to B a route to C
A
B
C
W
X
Y
legend:
customer
network:
provider
network
Suppose an ISP only wants to route traffic to/from its customer networks (does not want to carry transit traffic between other ISPs)

## Slide 56: BGP Export Policy
A announces path Aw to B and to C
B will not announce BAw to C:
  B gets no “revenue” for routing CBAw, since none of C, A, w are B’s customers
C will route CAw (not using B) to get to w
A
B
C
W
X
Y
legend:
customer
network:
provider
network
Suppose an ISP only wants to route traffic to/from its customer networks (does not want to carry transit traffic between other ISPs)

## Slide 57: BGP Import Policy
Suppose C announces path Cy to x
Further, y announces a direct path (“y”) to x
Then x may choose not to import the path Cy to y since it has a peer path (“y”) towards y
A
B
C
W
X
Y
legend:
customer
network:
provider
network
Suppose an ISP wants to minimize costs by avoiding routing through its providers when possible.

## Slide 58: Q2. BGP Route Selection
When a router imports more than one route to a destination IP prefix, it selects route based on:
  local preference value attribute (import policy decision -- set by network admin)
  shortest AS-PATH
  closest NEXT-HOP router
  Several additional criteria: You can read up on the full, complex, list of criteria, e.g., at https://www.cisco.com/c/en/us/support/docs/ip/border-gateway-protocol-bgp/13753-25.html

## Slide 59: Problems with BGP
Not designed for efficiency
Only a single path per destination
Slow to converge after a change
Vulnerable to bugs & malice
Nothing to do with path length, delay, or available capacity.