## Slide 1: Network Virtualization
Lecture 7
Srinivas Narayana
http://www.cs.rutgers.edu/~sn624/553-S23

## Slide 2
How to virtualize networking across a shared compute cluster?
A detour.

## Slide 3: Software/hardware layering at hosts
Link: best-effort local pkt delivery
Network: best-effort global pkt delivery
Transport: provide guarantees to apps
Application: useful user-level functions
Communication functions broken up and “stacked”
Each layer depends on the one below it.
Each layer supports the one above it.
The interfaces between layers are well-defined and standardized.

## Slide 4: Routing

## Slide 5: Two key network-layer functions
Forwarding: move packets from router’s input to appropriate router output
Routing: determine route taken by packets from source to destination
  routing algorithms
The network layer solves the routing problem.
Analogy: taking a road trip
Forwarding: process of getting through single exit
Routing: process of planning trip from source to destination
network
layer
runs
everywhere

## Slide 6: Control/Data Planes
Data plane = Forwarding
local, per-router function
determines how datagram arriving on router input port is forwarded to router output port
Control plane = Routing
network-wide logic
determines how datagram is routed along end-to-end path from source to destination endpoint
two control-plane approaches:
  Distributed routing algorithm running on each router
  Centralized routing algorithm running on a (logically) centralized machine
0111
values in arriving
packet header
1
2
3

## Slide 7: Distributed Routing

## Slide 8
Routing
Algorithm
data
plane
control
plane
1
2
0111
values in arriving
packet header, i.e, destination IP address
3
Data plane
per-packet processing
(~ tens of nanoseconds)
Control plane
Traditional routing protocols: per route-change processing
(~ a few tens of seconds)
Distributed routing

## Slide 9: What is the goal of routing?
Efficiency: find “good” paths
  Low latency, low cost, high bandwidth, etc.
  Often translates to shortest path on a suitably modeled graph!
  Edges: link metrics. Nodes: routers.
Internet rationale: distribute intelligence: avoid failures; scale
Two questions: (1) what messages? (2) what algorithm?
  Link state and distance vector protocols
  Applicable when
Example 1: link state routing protocol

## Slide 10: Q1: Information exchange
Link state flooding: the process by which neighborhood information of each network router is transmitted to all other routers
Each router sends a link state advertisement (LSA) to each of its neighbors
LSA contains the router ID, the IP prefix owned by the router, the router’s neighbors, and link cost to those neighbors
Upon receiving an LSA, a router forwards it to each of its neighbors: flooding
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5

## Slide 11: Q1: Information exchange
Eventually, the entire network receives LSAs originated by each router
LSAs put into a link state database
LSAs occur periodically and whenever the graph changes
  Example: if a link fails, or new router added
The routing algorithm running at each router can use the entire network’s graph to compute least cost paths
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
Q2: Algorithm: Dijkstra’s shortest paths
Destination IP prefix
Output Port on Router
Forwarding table

## Slide 12: Example 2: Internet Routing

## Slide 13: The Internet is a large federated network
AT&T
Comcast
Verizon

## Slide 14: The Internet is a large federated network
AT&T
Comcast
Verizon
Several autonomously run organizations (AS’es): No one “boss”
Organizations cooperate, but also compete
e.g., AT&T has little commercial interest in revealing its internal network structure to Verizon.

## Slide 15: The Internet is a large federated network
AT&T
Comcast
Verizon
Several autonomously run organizations: No one “boss”
Organizations cooperate, but also compete
Message exchanges must
not reveal internal network details.
Algorithm must work with “incomplete” information about its neighbors’ internal topology.

## Slide 16: The Internet is a large federated network
AT&T
Comcast
Verizon
Internet today: > 70,000 unique autonomous networks
Internet routers: > 800,000 forwarding table entries
Keep messages & tables as small as possible. Don’t flood
Algorithm must be incremental: don’t recompute the whole table on every message exchanged.

## Slide 17: Inter-domain Routing
The Internet uses Border Gateway Protocol (BGP)
All AS’es speak BGP. It is the glue that holds the Internet together
BGP is a path vector protocol
Distance vector protocols
Routing protocols
Link state
protocols
Path vector protocols
Messages?
Algorithm?
Applicable within a single AS

## Slide 18: (1) BGP Messages
Routing Announcements or Advertisements
  “I am here” or “I can reach here”
  Occur over a TCP connection (BGP session) between routers
Route announcement = destination + attributes
  Destination: IP prefix
Route Attributes:
  AS-level path
  Next hop
  Several others: origin, MED, community, etc.
An AS promises to use advertised path to reach destination
Only route changes are advertised after BGP session established
2b
2d
2c
2a
X
“I am here.”
Dst: 128.1.2.0/24
AS path: X
“I can reach X”
Dst: 128.1.2.0/24
AS path: AS2, X
AS 2
1b
1d
1c
1a
No link metrics, distances!
Exchange paths: path vector
Loop detection is easy
(no “count to infinity”)

## Slide 19: (2) BGP algorithm
A BGP router does not consider every routing advertisement it receives by default to make routing decisions!
  An import policy determines whether a route is even considered a candidate
Once imported, the router performs route selection
A BGP router does not propagate its chosen path to a destination to all other AS’es by default!
  An export policy determines whether a (chosen) path can be advertised to other AS’es and routers
Business policy considerations drive BGP.
Not necessarily efficient outcomes!
Programmed by network operator

## Slide 20: Policy arises from business relationships
Customer-provider relationships:
  E.g., Rutgers is a customer of AT&T
Peer-peer relationships:
  E.g., Verizon is a peer of AT&T
Business relationships depend on where connectivity occurs
  “Where”, also called a “point of presence” (PoP)
  e.g., customers at one PoP but peers at another
  Internet-eXchange Points (IXPs) are large PoPs where ISPs come together to connect with each other (often for free)

## Slide 21: BGP Export Policy
A,B,C are provider networks
X,W,Y are customers (of provider networks)
X is dual-homed: attached to two networks
policy to enforce: X does not want to route from B to C via X
  So, X will not announce to B a route to C
A
B
C
W
X
Y
legend:
customer
network:
provider
network
Suppose an ISP only wants to route traffic to/from its customer networks (does not want to carry transit traffic between other ISPs)

## Slide 22: BGP Export Policy
A announces path Aw to B and to C
B will not announce BAw to C:
  B gets no “revenue” for routing CBAw, since none of C, A, w are B’s customers
C will route CAw (not using B) to get to w
A
B
C
W
X
Y
legend:
customer
network:
provider
network
Suppose an ISP only wants to route traffic to/from its customer networks (does not want to carry transit traffic between other ISPs)

## Slide 23: BGP Import Policy
Suppose C announces path Cy to x
Further, y announces a direct path (“y”) to x
Then x may choose not to import the path Cy to y since it has a peer path (“y”) towards y
A
B
C
W
X
Y
legend:
customer
network:
provider
network
Suppose an ISP wants to minimize costs by avoiding routing through its providers when possible.

## Slide 24: Q2. BGP Route Selection
When a router imports more than one route to a destination IP prefix, it selects route based on:
  local preference value attribute (import policy decision -- set by network admin)
  shortest AS-PATH
  closest NEXT-HOP router
  Several additional criteria: You can read up on the full, complex, list of criteria, e.g., at https://www.cisco.com/c/en/us/support/docs/ip/border-gateway-protocol-bgp/13753-25.html

## Slide 25: Problems with BGP
Not designed for efficiency
Only a single path per destination
Slow to converge after a change
Vulnerable to bugs & malice
Nothing to do with path length, delay, or available capacity.
Approaches to bring flexibility:
Flexible control logic for path selection
(Google, Facebook)
Detour/overlay routing (Akamai)

## Slide 26: Example 3: Layer-2 switching

## Slide 27: Layer-2 switching
Switch: move packets based on link layer addresses
Provide an illusion of a single link connecting many endpoints
  Without every endpoint necessarily hearing every other endpoint
Learning switch: zero configuration or control plane.
  All endpoints in the same IP network
  Flood packets when dest MAC address unknown
  Use source MAC of incoming packets and associate with the incoming switch port: use later for forwarding
Works even if endpoints move, so long as they are in the same IP prefix

## Slide 28: Centralized Routing

## Slide 29: Problems with distributed control planes
Management decisions tied to distributed protocols
  Ex: Set OSPF link weights to force traffic through desired path
  Ex: Non-deterministic network state after a link failure
Data and control plane controlled by vendors: proprietary interfaces
?
X

## Slide 30: Traditional IP network
Data plane
Data plane
Data plane
Data plane
Control plane
Control plane
Control plane
Control plane

## Slide 31: Software-defined network
Data plane
Data plane
Data plane
Data plane
Logically-centralized control plane

## Slide 32: Software-Defined Networking

## Slide 33: SDN (1/2): Centralized control plane
Data plane
Data plane
Data plane
SDN controller
Data plane
Control planes lifted from switches
… into a logically centralized controller
… running in a compute cluster

## Slide 34: SDN (2/2): Open interface to data plane
Data plane
Data plane
Data plane
SDN controller
Data plane

## Slide 35: Some immediate consequences

## Slide 36: (1) Simpler switches
Data plane
Data plane
Data plane
Small set of hardware instructions.
SDN controller
Data plane

## Slide 37: Data plane primitive: Match-action rules
Match arbitrary bits in the packet header
  Match on any header, or new header
  Match exact, a subset (ternary), or over a range
  Allows any flow granularity
Actions
  Forward to port(s), drop, send to controller, count,
  Overwrite header with mask, push or pop, …
  Forward at specific bit-rate
Prioritized list of rules
Header
Data
Match: 1000x01xx01001x
Action: fwd(port 2)
Priority: 65500

## Slide 38: (2) Network programming abstractions
Data plane
Data plane
Data plane
Application
SDN Controller: Compiler + Run-Time
Application
Application
Write modular apps and compose them
Data plane

## Slide 39: (3) Formal verification of Network Policy
Data plane
Data plane
Data plane
Application (specified as code)
SDN Controller: Compiler + Run-Time
Data plane
Static checking
Dynamic
checking

## Slide 40: (4) Unified network operating system
Data plane
Data plane
Data plane
Application
Network Operating System
Application
Application
Separate distributed system concerns from expressing intent
Data plane
Persist app state
Graceful failover
Replication for perf
Consistent view

## Slide 41: New technical challenges of SDN
Availability: surviving failures of the controller
Controller scalability: many routers, many events
  Response time: Delays between controller and routers
Consistency: Ensuring multiple controllers behave consistently
Designing flexible router mechanisms
Compilation: translating intent to mechanisms
Verification: ensuring controller policy is faithfully implemented
Security: entire network owned if the controller is exploited
Interoperability: legacy routers; neighboring domains; …

## Slide 42: Virtualizing Networking in a Shared Cluster

## Slide 43: Typical network structure: Fat Trees
…
Rack
ToR switch
Agg switch
Spine switch
Capacities must increase as you go up the tree

## Slide 44: Networking in a multi-tenant cloud
Problems: Many tenants, time-varying demands.
  Want homogeneity across data center on use of compute capacity
  Where to provision VMs?
  How to migrate VMs or scale the number of VMs?
Idea (1): VMs get their own network addresses
  network address virtualization
Idea (2): tenants should be able to use custom topologies
  Facilitate migration, consistent view for monitoring and maintenance tools, etc.
  Needed “in practice” rather than “in principle”
  But, important to do!

## Slide 45: How cloud network looks to a tenant
Control abstraction: pipeline of lookup tables
Packet abstraction: send to IP addresses of your own
  Processed through switch/router topology
  Data plane behavior defined through control plane configuration
Design of NVP (nicira virtualization platform):
  Push all interesting data plane behaviors to the edge (hypervisor, OVS)
  The core of the network (switches/routers) just moves data using tunnel headers

## Slide 46: Topology and Address Virtualization
Topology virtualization
Address virtualization
(separation of tenant and provider addresses through tunneling)
Effect: Move packets from source vNIC to dest vNIC
Performance: Caching

## Slide 47: Controller design
Declarative design: language to specify tuples of rules/relations
  No need to implement a state machine to transition rule sets
  Use a compiler to emit correct, up to date logical datapaths (tuples)
Shared-nothing parallelism to scale
  Different logical datapaths easily distributed
  “Template” rules output from logical datapaths may be independently specialized to specific hypervisors and VMs
Controller availability maintained using standard leader election mechanisms
Control and data paths fail independently
  Existing OVS hypervisor rules can process packets even if controller fails
  Fast failover through precomputed failover installed in the data path

## Slide 48
Making old software use new networks usually means making new networks behave like old ones.