## Slide 1: Internet Architecture
Lecture 2
Srinivas Narayana
http://www.cs.rutgers.edu/~sn624/553-S25

## Slide 2: Some definitions
The Internet is an example of a computer network
Endpoint or Host: Machine running user application
Packet: a unit of data transmission (ex: 1500 bytes)
Link: physical communication channel between two or more machines
Router: A machine that processes packets moving them from one link to another towards a destination
Network: Collection of interconnected machines
Address: a unique name given to a machine
host/
endpoint
router
router
link
link
link
host/
endpoint
packet
IP: 10.0.0.1
IP: 128.0.0.2

## Slide 3: Some fundamental problems

## Slide 4: (1) Routing
Networks must move data between different hosts
Need to figure out how to move packets from one host to another host, e.g., how to reach google.com from your laptop
Known as the routing problem
Router
Router
Router

## Slide 5: (2) Name Resolution
Routing effectively requires locating the endpoints appropriately
  Memory, speed, reactivity
Internet addresses allocated hierarchically
  Machine readable, not easy for humans to remember
Link addresses are tied to the hardware on the endpoint
Name resolution: how to turn human-readable names (google.com) into routable addresses?
Zipcode 08854
Zipcode 08090

## Slide 6: In general, networks give no guarantees
Packets may be lost, corrupted, reordered, on the way to the destination
  Best effort delivery
Advantage: The network becomes very simple to build
  Don’t have to make it reliable
  Don’t need to implement any performance guarantees
  Don’t need to maintain packet ordering
  Almost any medium can deliver individual packets
    Example: RFC 1149: “IP Datagrams over Avian Carriers”
Early Internet thrived: easy to engineer, no guarantees to worry about

## Slide 7: Providing guarantees for applications
How should endpoints provide guarantees to applications?
Transport software on the endpoint oversees implementing guarantees on top of an unreliable network
Reliable delivery, ordered delivery, fair sharing of resources

## Slide 8: (3) Congestion control
How quickly should endpoints send data?
Known as the congestion control problem
Congestion control algorithms at source endpoints react to remote network congestion. Part of the transport sw/hw stack.
Key question: How to vary the sending rate based on network signals?

## Slide 9: (4) High-Speed Interconnect
Transport won’t help if the network has choke points: e.g., routers
The interconnection problem: how do you design routers to achieve high end-to-end performance between endpoints?
  Also designing large data center networks
Data Center

## Slide 10: Layering and Protocols

## Slide 11: Software/hardware organization at hosts
Link: best-effort local pkt delivery
Network: best-effort global pkt delivery
Transport: provide guarantees to apps
Application: useful user-level functions
Communication functions broken up and “stacked”
Each layer depends on the one below it.
Each layer supports the one above it.
The interfaces between layers are well-defined and standardized.

## Slide 12
Internet software and hardware
are arranged in layers.
Layering provides modularity
Each layer: well-defined function
& interfaces to layers above & below it.
Functionality is implemented in protocols.

## Slide 13: Protocols: The “rules” of networking
Protocols consist of two things
Message format
  structure of messages exchanged with an endpoint
Actions
  operations upon receiving, or not receiving, messages
Example of a Zoom conversation:
  Message format: English words and sentences
  Actions: when a word is heard, say “yes”; when nothing is heard for more than 3 seconds, say “can you hear me?”

## Slide 14: The protocols of the Internet
Standardized by the Internet Engineering Task Force (IETF)
  through documents called RFCs (“Request For Comments”)
Layering of protocols
…
FTP
HTTP
SIP
RTSP
TCP
UDP
IP
802.11
X.25
ATM
HTTPS
HTTP
FTP
TFTP
NV
TCP
UDP
IP
Ether
ATM
WiFi
…

## Slide 15
Link layer
Network
Transport
Applications
The Internet
Link layer
Network
Transport
Applications
The Internet
Packet takes on headers (metadata) at each layer
Packet starts as an
app “payload”

## Slide 16
Link layer
Network
Transport
Applications
Link layer
Network
Transport
Applications
Link layer
Network
Link layer
Network

## Slide 17
Link layer
Network
Transport
Applications
Link layer
Network
Transport
Applications
Link layer
Network
Link layer
Network
Routers have network and link layers too!

## Slide 18: Layering
Communication over the Internet is a complex problem.
Layering simplifies understanding, testing, maintaining
Easy to improve or replace protocol at one layer without affecting others

## Slide 19: Name Resolution

## Slide 20
Google
google.com
Machines communicate using IP addresses and ports
IP addresses: ~12 digits (IPv4) or more
Ports: fixed based on application (e.g., 80: web)
Need a way to turn human-readable addresses into Internet addresses.
Ask someone
Ask everyone
Tell everyone
Directory service
Query broadcast
Information flooding
Asking “someone” could involve asking many machines…

## Slide 21: Domain Name Service
Key idea: Implement a server that looks up a table.
Will this scale?
  Every new (changed) host needs to be (re)entered in this table
  Performance: can the server serve billions of Internet users?
  Failure: what if the server or the database crashes?
  Security: What if someone “takes over” this server?
DOMAIN NAME | IP ADDRESS
spotify.com | 98.138.253.109
cs.rutgers.edu | 128.6.4.2
www.google.com | 74.125.225.243
www.princeton.edu | 128.112.132.86
QUERY cs.rutgers.edu
RESPONSE 128.6.4.2
<Client IP, CPort, DNS server IP, 53>
<DNS server, 53, Client IP, Cport>

## Slide 22: Distributed and hierarchical database
Root DNS Servers
com DNS servers
org DNS servers
edu DNS servers
rutgers.edu
DNS servers
umass.edu
DNS servers
google.com
DNS servers
amazon.com
DNS servers
wnyc.org
DNS servers
cs.rutgers.edu DNS server
RFC 1034
Top-level domain (TLD) servers
Authoritative name server
Hierarchy
Replication
Indirection

## Slide 23: DNS name resolution
requesting host
cs.rutgers.edu
gaia.cs.umass.edu
root DNS server
local DNS server
dns.rutgers.edu
1
2
3
4
5
6
umass.edu DNS server
dns.umass.edu
7
8
.edu DNS server
Host at cs.rutgers.edu wants IP address for gaia.cs.umass.edu
Local DNS server
Root DNS server
TLD DNS server
Authoritative DNS server

## Slide 24: DNS caching
requesting host
cs.rutgers.edu
gaia.cs.umass.edu
root DNS server
local DNS server
dns.rutgers.edu
1
2
3
4
5
6
umass.edu DNS server
dns.umass.edu
7
8
.edu DNS server
Once (any) name server learns a name to IP address mapping, it caches the mapping
Cache entries timeout (disappear) after some time
TLD servers typically cached in local name servers
In practice, root name servers aren’t visited often!
Caching is pervasive in DNS

## Slide 25: Example DNS interactions
dig <domain-name>
dig +trace <domain-name>
dig @<dns-server> <domain-name>

## Slide 26
Google
google.com
The web is a specific application protocol running over a network: HyperText Transfer Protocol (HTTP)
Objects
Each object addressable by a name (URL)
Named objects can be static (image, video)
… or the result of a dynamic app process

## Slide 27: Web interactions
Hostname | IP address
Google.com | 10.0.1.2
Host name
Server IP Address
DNS server
clientIP, clientPort, server IP Address, 80
HTTP messages
(HTTP application typically associated with port 80)
HTTP request
HTTP response
I want to browse google.com

## Slide 28: Example HTTP interactions
wget google.com (or) curl google.com
telnet example.com 80
  GET / HTTP/1.1
  Host: example.com
(followed by two enter’s)
Exercise: try
  telnet google.com 80
  telnet web.mit.edu 80

## Slide 29: Remembering users: cookies
client
server
http request msg + auth
http response +
Set-cookie: 1678
http request (no auth)
cookie: 1678
Personalized http response
http request (no auth)
cookie: 1678
Personalized http response
cookie-
specific
action
cookie-
specific
action
server
creates ID
1678 for user
entry in backend
database
access
access
Cookie file
Amazon: 1678
Cookie file
Amazon: 1678
Cookie file
Amazon: 1678
one week later:
Netflix: 436
Netflix: 436
Netflix: 436
Cookie is typically opaque to client.

## Slide 30: Improving performance: Web caching
GET foo.html
Web Server
(also called origin server in this context)
Clients
Web cache
GET foo.html
Store foo.html
on receiving response
Network administrators (e.g., Rutgers) may run web caches to remember popular web objects
Hit: cache returns object
Miss: obtain object from originating web server (origin server) and return to client
  Also cache the object locally
Reduce response time
Reduce traffic requirements (and $$) on an organization’s network connections
The Internet
Return cached object!
Rutgers

## Slide 31: Not all content is effectively cacheable
Personalized content
Interactive processing
  e.g., forms, shopping carts, ajax, etc.
Long tail of (obscure) content