## Slide 1: Hardware-Software Co-Design for Network Performance Measurement
Srinivas Narayana
MIT CSAIL

## Slide 2: An example: High tail latencies
Delay completion of flows
(and applications)
Notes: Applications and network operators today care about the problem of high tail latencies.
When an app spawns multiple flows, it is important that all of them finish quickly, in order to respond quickly to a user request.
If even some flows are delayed, the user response may be delayed or of lower quality.

## Slide 3: An example: High tail latencies
Where is the queue buildup?
How did queues build up?
UDP on-off traffic?
Fan-in of short flows?
Which other flows cause queue buildup?
On-off  Throttle UDP
Fan-in  Change traffic pattern

## Slide 4: An example: High tail latencies
Where is the queue buildup?
How did queues build up?
UDP on-off traffic?
Fan-in of short flows?
Which other flows cause queue buildup?
On-off  Throttle UDP
Fan-in  Change traffic pattern
What measurement support do you need?

## Slide 5: Network performance questions
Transport protocol diagnoses
  Fan-in problems (incast and outcast)
  Incidents of reordering and retransmissions
  Interference from bursty traffic
Flow-level metrics
  Packet drop rates
  Queue latency EWMA per connection
  Incidence and lengths of flowlets
Network-wide questions
  Route flapping incidents
  High end to end latencies
  Locations of persistently long queues
...
Notes: Hari: Try to categorize / put structure
Understanding congestion control: Ns2/ns3  bullet point seems redundant, since others capture it.
Consider swapping this slide with existing measurement support – can talk abstractly about the latter then. Can talk about why the approaches don’t work for a _class_ of problems, not just one…
-- possible categorizations:
Source of information used
Nature of problem (e.g., switch-level, flow-level, network-wide, ...)
Latency, loss, ...

## Slide 6: Existing measurement approaches
Sampling (netflow, sflow)
Endpoint solutions (pingmesh, etc.)
Counting (opensketch, etc.)
Packet capture (endace, niksun, etc.)
Misses events
End-to-end; lack direct visibility
No visibility into queues
Not everywhere & always
Notes: TODO: add a “cross” mark to indicate the approach doesn’t really work

## Slide 7
Can we build better
performance monitoring tools
for networks? 

## Slide 8: Contributions
Declarative performance query language
  Extract primitives from use cases
  Abstract table of performance for all packets at all queues
  SQL-like queries on this table
Hardware design for performance measurement
  Precise visibility at line rates of 10-100 Gb/s per port
  Programmable key-value store
Compiler: work in progress
  Go from high-level queries to switch configuration
Co-Design Hardware & Software

## Slide 9: Performance query system
Network operator
Diagnostic apps
Declarative performance queries
Accurate query results at low overhead
Notes: Cat picture credit: http://www.cathub.tv/13-cats-using-computers-will-surprise-humans/
Code picture credit: http://www.lifehacker.com.au/2011/10/turn-your-desktop-into-an-ode-to-code-with-these-wallpapers/
Have this after the contributions slide to make it clearer from point of view of users/applications. ”what the system allows you to do”. Should be very brief.
First flow to try: have contributions slide, then this high-level overview, then the query language & hardware design, then talk about the design philosophy of “co-design” (or iterative design/joint design etc.)

## Slide 10
Performance Query Language
Notes: (here around 4.5 minutes… seems fine.)

## Slide 11: (1) Declarative language abstraction
Write SQL-like performance queries on an abstract table:
(Packet headers,
Queue id,
Queue size,
Time at queue ingress,
Time at queue egress,
Packet path info)
For all packets at all queues
Notes: Approach to introduce language: introduce the solution (not enough time to go through semantic features needed). Emphasize what is unique about the solution e.g., this is not exactly SQL because <yada yada>…

## Slide 12: (1) Performance query examples
Queues and traffic sources with high latency
SELECT srcip, qid FROM T WHERE tout – tin > 1ms
Focus on packets with specific performance

## Slide 13: (1) Performance query examples
Traffic counts per connection
SELECT 5tuple, count GROUPBY 5tuple
Aggregation function

## Slide 14: (1) Performance query examples
Queue latency EWMA by connection
SELECT 5tuple, qid, ewma GROUPBY 5tuple, qid
def ewma (lat_est, (tin, tout)):
lat_est = (1-alpha) * lat_est + alpha * (tout-tin)
User-defined aggregation function

## Slide 15: (1) Performance query examples
Queue latency EWMA by connection
SELECT 5tuple, qid, ewma GROUPBY 5tuple, qid
def ewma (lat_est, (tin, tout)):
lat_est = (1-alpha) * lat_est + alpha * (tout-tin)
Fold functions with bounded state
Packet-order-dependent
function (unlike SQL)
Notes: Packet-order-dependent: more recent queueing delays are more significant than ones in the past.

## Slide 16: (1) Performance query examples
Queue latency EWMA by connection
SELECT 5tuple, qid, ewma GROUPBY 5tuple, qid
def ewma (lat_est, (tin, tout)):
lat_est = (1-alpha) * lat_est + alpha * (tout-tin)
Fold functions with bounded state: guided by hardware feasibility
Packet-order-dependent
function (unlike SQL)
Notes: Packet-order-dependent: more recent queueing delays are more significant than ones in the past.

## Slide 17: (1) Performance query examples
Language also enables composing multiple queries through JOINs
See paper for more examples

## Slide 18
Hardware for Performance Measurement
Notes: (Here around 9.5 minutes…)

## Slide 19: (2) Existing features useful!
Egress pipeline
Ingress pipeline
match/action
match/action
match/action
match/action
Queues/
Scheduler
WHERE predicates as match-action rules
Queue length & pkt timestamps: metadata fields
What remains: GROUPBY!
Notes: Existing features are already useful.
For example, the queueing components can already expose performance information like queue sizes and timestamps as metadata headers on packets as they are processed.
Picture credit: Anirudh Sivaraman

## Slide 20: (2) Hardware support for aggregation
SELECT 5tuple, ewma GROUPBY 5tuple
5tuple | ewma
… | 
Want:
Key-value store with
read-modify-write ops

## Slide 21: (2) Challenges in building switch KV
Fast: Run at line rate
  1GHz packet rate
Big: Scale to millions of keys
  e.g., number of connections
Existing memories aren’t fast and big enough!

## Slide 22: (2) Solution: Caching?
Key
Value
Packet with incoming key K
Key
Value
On-chip cache (SRAM)
Off-chip backing store (DRAM)
Request key K
Respond K, V’’
K
V’’
Notes: Think of a natural solution of using a smaller but faster “cache”, with a slower but larger off-chip store with all the key-value pairs.
Arriving here 2 minutes after starting hardware section.

## Slide 23: (2) Solution: Caching?
Key
Value
Packet with incoming key K
Key
Value
On-chip cache (SRAM)
Off-chip backing store (DRAM)
Request key K
Respond K, V’’
K
V’’
K
V’’
Notes: Think of a natural solution of using a smaller but faster “cache”, with a slower but larger off-chip store with all the key-value pairs.
Arriving here 2 minutes after starting hardware section.

## Slide 24: (2) Solution: Caching?
Key
Value
Packet with incoming key K
Key
Value
On-chip cache (SRAM)
Off-chip backing store (DRAM)
Request key K
Respond K, V’’
K
V’’
Q: Multiple packets with cache misses?
K
V’’
Notes: But if there are multiple packets arriving one after another, and they all miss, the DRAM can’t support memory bandwidth of 1GHz.

## Slide 25: (2) Solution: Caching?
Key
Value
Packet with incoming key K
Key
Value
On-chip cache (SRAM)
Off-chip backing store (DRAM)
Request key K
Respond K, V’’
K
V’’
Q: Multiple packets with cache misses?
Packet processing must wait for DRAM,
but DRAM can’t keep up with accesses at 1Ghz!
Notes: But if there are multiple packets arriving one after another, and they all miss, the DRAM can’t support memory bandwidth of 1GHz.

## Slide 26: (2) A different cache design
Key
Value
Packet with incoming key K
Key
Value
On-chip cache (SRAM)
Off-chip backing store (DRAM)
Notes: One additional minute from last checkpoint.

## Slide 27: (2) A different cache design
Key
Value
Packet with incoming key K
Key
Value
On-chip cache (SRAM)
Off-chip backing store (DRAM)
Evict key K’, V’
K’
V’’
K
V0

## Slide 28: (2) A different cache design
Key
Value
Packet with incoming key K
Key
Value
On-chip cache (SRAM)
Off-chip backing store (DRAM)
Evict key K’, V’
K’
K
V0
Merge V’ (cache) and V’’(store)
(nothing comes back)

## Slide 29: (2) A different cache design
Key
Value
Packet with incoming key K
Key
Value
On-chip cache (SRAM)
Off-chip backing store (DRAM)
Evict key K’, V’
K’
Merge V’ (cache) and V’’(store)
Q: Multiple packets with cache misses?

## Slide 30: (2) A different cache design
Key
Value
Packet with incoming key K
Key
Value
On-chip cache (SRAM)
Off-chip backing store (DRAM)
Evict key K’, V’
K’
Merge V’ (cache) and V’’(store)
Q: Multiple packets with cache misses?
K
V0
K2
V0
K3
V0
K4
V0
Multiple cache evictions to merge

## Slide 31: (2) A different cache design
Key
Value
Packet with incoming key K
Key
Value
On-chip cache (SRAM)
Off-chip backing store (DRAM)
Evict key K’, V’
K’
Merge V’ (cache) and V’’(store)
Q: Multiple packets with cache misses?
K
V0
K2
V0
K3
V0
K4
V0
Multiple cache evictions + merges
Packet processing doesn’t wait for DRAM.
Retain 1GHz packet processing rate!👍

## Slide 32: (2) Can you always merge correctly?
In general, no!
Cache “forgets” the true value (in DRAM) after key eviction
However, merging is possible for some operations
Notes: If you walked through the standard approach of reading back latest cache values, and then explained our design … then this should be obvious. Do local updates and then merge later ... This question will come up naturally then. Turns out for a class of operations, yes; in general no.

## Slide 33: (2) The linear-in-state condition
Updates of the following form are mergeable:
S = A * S + B
A, B are functions of a bounded number of packets into the past
Examples:
  Packet and byte counters
  EWMA update
  (See others in paper)
Notes: We’ll talk about EWMA, as an example of how the merge happens.

## Slide 34: (2) EWMA example
SELECT 5tuple, qid, ewma GROUPBY 5tuple, qid
def ewma (lat_est, (tin, tout)):
lat_est = (1-alpha) * lat_est + alpha * (tout-tin)
State variable lat_est
Update satisfies S = A*S + B
A = 1-alpha
B = alpha*(tout-tin) for each packet

## Slide 35: (2) Merging EWMA evictions
Evicted K’, V’
Key
Value
K’
Merge operation:
V’’ = V’ - AnV0 + AnV’’
(n: #pkts that updated V’)
V’’
SELECT 5tuple, qid, ewma GROUPBY 5tuple, qid
Key
Value

## Slide 36
Is the system design feasible?
Notes: 2:45 after last checkpoint.

## Slide 37: Is the system design feasible?
Cache design feasibility
  Hash-based lookup
  Value update operations
  Cache eviction logic
  SRAM area
Backing store feasibility
  Tuples/second processed
Match-action, mirroring, …
Multiply-accumulate instruction; Domino
LRU processor caches
Tradeoff: Trace-driven evaluation
Notes: I won’t be discussing the details of the hardware itself. But most components are already implemented in other computer systems. We don’t expect show stoppers.
There are limits on how much memory we can provision for the cache on chip. Will the processing overhead at the backing store be reasonable at such memory sizes? We perform a trace-driven evaluation to find out.
-----------------
Could cut this if needed.
“obviously we haven’t build any hardware yet, but thought totally carefully, but there are no big show-stoppers…”
Components have all been built in hardware in other contexts. Have the slide but don’t need to walk through each.
SK: mention that we’ve done some trace-driven evaluations to measure cache eviction rates, etc. Evaluation with CAIDA trace  evaluation we did is that with a small enough cache of 2.5% memory, we can already process the updates to the backing store.
Add one picture from the evaluation  benefits of the architecture in terms of reducing the load on the backend processing system. Not send every packet to the dram for merging.
Put one result (x times reduction relative to shipping off every packet to the DRAM). More important point is that the backend data rate is low enough & area overhead is small enough. We have reduced it relative to a baseline where you send everything to a dram...
The specific numbers of tuples/sec etc. depend on the workload. “Preliminary evaluation” of feasibility with X SRAM and Y workload; you need a backend that has ZZ updates/sec. Could even be a standard KV store memcached/redis. 32Mbit is doable in hardware today... 2.5% area overhead relative to chip.
what does “per switch” mean? 64X10Gb/s switch... At 30% utilization, processing 800K tuples per second is enough. Probably just 1-2 memcached servers for each switch.
-- citations for the few hundreds of 1000s of ops per second per core in the blogs.
-- 22.6M average sized packets per second is our traffic. 22.6 * 850 * 8 = 153,680 Mbits per second = 153 Gb/s that you can sustain using a few memcached cores.
Modern data center today: one multi-core server for several racks. Few cores can handle this much...
More important to explain what the test was and the parameters to put the numbers in context. People may not get hung up on the numbers.
64 servers at 10Gbit/s -> couple of cores to process the backend traffic
1:64 ratio of monitoring servers to processing servers ... In practice probably even smaller (since multiple racks for each server). Overhead in terms of more servers is like 1-2%.
Tetration: 1% additional capex for servers isn’t that much if it gives you that much more visibility.
800K * 128 bits / sec = 1280 Kbits/sec = 102 Mbits/sec ~ about 1% of the bandwidth of the link itself! Useful.

## Slide 38: Cache area & Eviction processing
Q: Can evictions be processed for “reasonable” cache sizes?
CAIDA traffic trace with ~150 million packets
  Switch with 64 port 10Gb/s switch
Typical data center utilization and packet sizes [Benson et al.]
Notes: Could cut this if needed.
“obviously we haven’t build any hardware yet, but thought totally carefully, but there are no big show-stoppers…”
Components have all been built in hardware in other contexts. Have the slide but don’t need to walk through each.
SK: mention that we’ve done some trace-driven evaluations to measure cache eviction rates, etc. Evaluation with CAIDA trace  evaluation we did is that with a small enough cache of 2.5% memory, we can already process the updates to the backing store.
Add one picture from the evaluation  benefits of the architecture in terms of reducing the load on the backend processing system. Not send every packet to the dram for merging.
Put one result (x times reduction relative to shipping off every packet to the DRAM). More important point is that the backend data rate is low enough & area overhead is small enough. We have reduced it relative to a baseline where you send everything to a dram...
The specific numbers of tuples/sec etc. depend on the workload. “Preliminary evaluation” of feasibility with X SRAM and Y workload; you need a backend that has ZZ updates/sec. Could even be a standard KV store memcached/redis. 32Mbit is doable in hardware today... 2.5% area overhead relative to chip.
what does “per switch” mean? 64X10Gb/s switch... At 30% utilization, processing 800K tuples per second is enough. Probably just 1-2 memcached servers for each switch.
-- citations for the few hundreds of 1000s of ops per second per core in the blogs.
-- 22.6M average sized packets per second is our traffic. 22.6 * 850 * 8 = 153,680 Mbits per second = 153 Gb/s that you can sustain using a few memcached cores.
Modern data center today: one multi-core server for several racks. Few cores can handle this much...
More important to explain what the test was and the parameters to put the numbers in context. People may not get hung up on the numbers.
64 servers at 10Gbit/s -> couple of cores to process the backend traffic
1:64 ratio of monitoring servers to processing servers ... In practice probably even smaller (since multiple racks for each server). Overhead in terms of more servers is like 1-2%.
Tetration: 1% additional capex for servers isn’t that much if it gives you that much more visibility.
800K * 128 bits / sec = 1280 Kbits/sec = 102 Mbits/sec ~ about 1% of the bandwidth of the link itself! Useful.

## Slide 39: Cache area & Eviction processing
Key
Value
32 Mbit cache (2.5% switch area overhead)
Key
Value
Memcached/Redis on x86 servers
(1-2 cores!)
800K tuples/sec

## Slide 40: Cache area & Eviction processing
Key
Value
32 Mbit cache (2.5% switch area overhead)
Key
Value
Memcached/Redis on x86 servers
(1-2 cores!)
800K tuples/sec
Monitor a 64-server rack (10Gb/s)
with just 1-2 cores.

## Slide 41: Takeaways
Switches: precise performance visibility at line rate
Co-design: build flexible hardware with the right language interfaces
Notes:   Examples of flexible hardware/restricted language:
  Generalized packet-order-dependent UDFs
  Restricted joins
1:30 since last checkpoint.